INSTRUCTIONS FOR PREPARING A

STORMWATER POLLUTION PREVENTION PLAN (SWPPP)

This document presents a template for assembling a Stormwater Pollution Prevention Plan (SWPPP) for public improvement projects administered by the City of Overland Park’s Public Works Department. The City does not require that this exact format be used, but a SWPPP must be present on all jobs that hold a City Land Disturbance Permit and a Kansas Department of Health and Environment (KDHE) Construction Site Erosion Control permit.

The SWPPP is to be assembled in a 3-ring binder, with four (4) tab dividers for the following sections:

	Section 1:  Project Narrative

	Section 2:  Regulatory Permits

	Section 3:  Drawings

	Section 4:  Construction Phase Forms

The template includes a SWPPP cover sheet, table of contents, and section cover sheets with applicable content. General descriptions and instructions are included on the cover sheet of each section to clarify the purpose and intent.

Sections 1, 2, and 3 are the components of the SWPPP that will be assembled by the City (or City’s Consultant). The SWPPP will be assembled for the project and provided to the Contractor at the pre-construction meeting. A copy of the SWPPP, labeled “Copy of SWPPP”, will be provided to the City’s Construction Inspector. Presented on the following page is a checklist of the components the SWPPP document should include for pre-construction activities.

Section 4 includes forms related to the maintenance of the SWPPP which is the responsibility of the Contractor.

Stormwater Pollution Prevention Plan (SWPPP)

Checklist for Pre-Construction Activities

| □ | Prepare SWPPP before construction starts |
| --- | --- |
| Include in Site Description: |
| □ | - Nature of activity in description |
| □ | - Intended sequence of major activities |
| □ | - Total disturbed acreage |
| □ | - General location map |
| □ | Site map that shows drainage patterns, slopes, areas of disturbance, locations of major controls, structural practices shown, stabilization practice, offsite materials, waste, borrow or equipment storage areas, surface waters, discharge points, area of final stabilization |
| □ | Description of all pollution control measures |
| □ | Description of implementation sequence |
| □ | Description of interim stabilization practices |
| □ | Description of permanent stabilization practices |
| □ | Description of a sequence to implement stabilization practices |
| □ | Describe structural practices that are diverting flow from exposed soils, retaining flows, or limiting runoff from exposed areas |
| □ | Describe measures that will be installed during the construction process to control pollutants in stormwater discharges that will occur AFTER construction operations have been completed |
| □ | Describe measure that will prevent discharge of solid materials to waters of the U.S. except as authorized by a 404 permit |
| □ | Describe measures to minimize off-site vehicle tracking and generation of dust |
| □ | Documentation from requirements of the Endangered Species Act |

STORM WATER POLLUTION

PREVENTION PLAN

#### [PROJECT NAME]

#### [CITY PROJECT NUMBER]

[Site Address]

#### Overland Park, Kansas

#### [Zip Code]

Prepared for:

City of Overland Park

8500 Santa Fe Drive

Overland Park, Kansas 66212

Prepared by:

[Preparer Name]

[Prepare Business]

[Preparer Address]

[Preparer City, State Zip Code]

[Preparer Phone No.]

#### [Month, Year]

# TABLE OF CONTENTS

###### SECTION 1:  PROJECT NARRATIVE

1.	Project and Site Description

2.	Best Management Practices

2.1	Coordination with Construction Activities

2.2	 Erosion Control Measures

2.3	 Sediment Control Measures

2.4	Chemical and Waste Control Measures

# SECTION 2:  REGULATORY PERMITS

Notice of Intent (NOI) Submitted to KDHE

KDHE Issued Permit Letter and Permit Number

KDHE General Permit for Construction

KDWP/KSHS Clearance Letters [if applicable]

Federal Permits [if applicable]

City of Overland Park Land Disturbance Permit

Adjacent Cities Land Disturbance Permits [if applicable]

###### SECTION 3: DRAWINGS

Vicinity Map

Erosion and Sediment Control Plans and Specifications

Site Map

SECTION 4: CONSTRUCTION PHASE FORMS

Construction/Implementation Checklist

Contractor Certification Form

Contractor’s Project Schedule

Potential Construction Site Stormwater Pollutants

Initial Inspection Report Form

Regular Inspection Report Form

BMP Checklist

Quality Assurance Inspection Form

Final inspection Form

Notice of Termination (NOT)

Optional:

SWPPP Modification Report Form

Project Rainfall Log Form

Amendment Form

SECTION 1

This section describes nature and sequence of construction activity, site features and sensitive areas to be protected, potential sources of pollution, and a general description and intent of erosion and sediment control BMPs to be implemented.  Elements of this section are intended to be project specific and provide adequate information about the project.

SECTION 1:  PROJECT NARRATIVE

1.	Project and Site Description

The City of Overland Park, Kansas is currently preparing construction plans for [insert project name]. The project involves the construction of [provide general description (i.e. road widening, storm drainage improvements, road or bridge construction, etc] for the purpose of [describe purpose and need of project].  Construction activities will commence [provide approximate start date] with an estimated completion date of [provide approximate end date]. Presented in Section 4 of this document is the Contractor’s project schedule.

The project site is located at [provide street address, nearest cross streets or general location] in the [provide legal site description: QTR, Section, Township and Range] in Johnson County, Overland Park, Kansas. The total area of the site is [XXX] acres.

Existing site conditions include [describe current land use]. The site has soils, which are classified by the USDA Natural Resources Conservation Service as [enter soil classification].  These soils are described as [enter description]. Existing vegetation consists of [describe vegetation] located [where onsite].

Runoff from the project site is discharged into [describe whether city storm drain, stream, river, etc.; how many major points of discharge on site; and ultimate receiving water body of site].  [This paragraph should also include identification of unique site features that may present erosion and sediment control challenges/concerns including streams, stream buffers, wetlands, steep slopes, or highly erodible soils]

There are [X] major phases of the construction work: [Describe the intended construction sequencing and timing of major activities, including grading activities, road and utility installation, and building phases.]

The estimated total area to be disturbed is [XXX] acres.  Soil disturbing activities will primarily include [describe general sequence of activities within each phase, i.e. site grading, installation of storm sewer pipes, inlets, construction of curb & gutters, utilities, retaining walls, etc.]. The primary potential sources of stormwater contamination for this project include soil disturbing activities and construction material spillage [edit this statement as needed to include additional pollutants].

2.	 Best Management Practices

The purpose of this section is to identify the types of erosion and sediment controls used during construction activities. The locations and details of these Best Management Practices (BMPs) are included in Section 3 (see Erosion and Sediment Control Plans). This section also addresses the control of other potential storm water pollutant sources.

2.1	Coordination with Construction Activities.   The Contractor will be responsible for implementing and maintaining the Best Management Practices (BMPs) through the course of construction. All BMPs shall be sequenced according to activities in the field as follows:

[Add, revise or delete the following bullets in blue font as needed to summarize general sequence of project]

a)	Through each phase of construction, natural areas and features will be protected from disturbance by placement of [insert method (i.e. signs, construction fence, etc).]

b)	Clearing and grading will not occur in an area until it is necessary for construction to proceed (see Project Phasing).

c)	Temporary perimeter sediment controls will be installed before any clearing and grading begins.

d)	The stabilized construction site entrance will be constructed before clearing and grading begins.

e)	Within 14 days of clearing and grading, areas not immediately affected by construction activities will be stabilized.

f)	Soil stockpiles will be stabilized no later than 14 days from the last construction activity in that area.

g)	Once earthwork activities ceases permanently in an area, that area will be stabilized

h)	 [A sediment basin or sediment trap at (indicate location)] will be constructed before any construction begins. All cleared and graded soils will be sloped to the sedimentation basin].

i)	 [After the entire site is stabilized, the accumulated sediment will be removed from the basin.  The sediment basin may be converted to a post construction BMP, as appropriate]

j)	[Vegetated swales, bio-retention cells, and other post construction infiltration BMPs will not be constructed until the entire site is stabilized.]

2.2	Erosion Control Measures.  The following BMPs will be used to stabilize onsite soils and prevent erosion during construction:

[Add, revise or delete the following bullets in blue font as needed to summarize purpose of BMP selected]

a)	[Permanent seeding and sodding, temporary seeding, hydroseeding, hydrocover, mulch cover] of disturbed areas when construction activities have temporarily or permanently ceased.

b)	Mulch Cover of disturbed areas when ground cover is required and temporary or permanent seeding is not feasible.

c)	[Erosion Control blankets, turf reinforcement mats, tackifiers, etc.] to provide temporary or permanent cover and/or stability to disturbed slopes or channels subject to overland or concentrated surface flow.

d)	Surface Roughening by means of grooving, tracking, disking or ripping of any rough graded slopes not yet ready for seeding or other treatment and which will not be disturbed for a period of 7 days.

e)	Effective dust control measures such as adequate moisture content or approved dust suppressants shall be taken.

2.3	Sediment Control Measures.  The following structural BMPs will be utilized to detain, filter or cause settlement of sediment from runoff, as well as measures used to temporarily direct or divert runoff onsite or at the site perimeter.

[Add, revise or delete the following bullets in blue font as needed to summarize purpose of BMP selected]

a)	[Silt fence, straw wattles, berms, dikes, gravel bags, filter socks etc.] will be used as temporary perimeter sediment controls to divert or detain flows from exposed soils and limit runoff and discharge of pollutants from exposed areas of the site.

b)	 [Temporary slope drains, berms, etc] shall be used to convey concentrated water from the top of a slope to the toe and thereby preventing erosion over the slope face.

c)	[Rock barriers, gravel bags, ditch checks, etc.] will be used in ditches with large or concentrated flows.

d)	[Wattles, foam dike, rock ditch checks, gravel bags, etc] will be placed to protect all storm sewer inlets and outlets on or near the site by filtering or temporarily impeding the flow sufficiently to reduce the quantity of sediment carried.

e)	Accumulated sediment behind barriers, traps, etc., shall be removed when it exceeds the volumes specified for any particular measure.

f)	   A temporary crossing shall be constructed to allow construction access and crossing of [name of creek].

2.4	Chemical and Waste Control Measures.   Presented in Section 4 of this document is a table summarizing the materials or substances with known hazardous properties that are expected to be present on site during construction.

Management of materials and practices, outside of soil disturbing activities, shall be the responsibility of the Contractor.  Such activities shall include, but not be limited to, the items shown below:

a)	Waste Disposal - All waste materials will be collected and stored in securely lidded metal dumpsters.  The dumpster will meet all local and state solid waste management regulations.  All waste and construction debris from the site will be deposited in the dumpsters.  The dumpster will be emptied on a periodical basis.  No construction waste materials will be buried onsite.

b)	Sanitary Waste - All sanitary waste will be collected from the portable units on a frequent, periodical basis by a licensed sanitary waste management contractor.

c)	Concrete Waste From Concrete Trucks - Excess concrete and concrete wash water shall be returned to the concrete plant or deposited at a designated containment area on site, constructed in a manner to prevent run-off from entering the street, storm water drainage systems or waterways.  Wash water may not be deposited in streets, curbs, gutters, storm drains, or waterways.

d)	Hazardous Substances and Hazardous Waste - All hazardous waste materials will be disposed of in the manner specified by local or state regulation or by the manufacturer.

SECTION 2

Include the following permits in this section:

a)	Notice of Intent (NOI) Submitted to KDHE (including attachments and figures, etc.)

b)	Copy of KDHE Issued Permit Letter and Permit Number

c)	Copy of KDHE General Permit for Construction

d)	Copy of KDWP/KSHS Clearance Letters (if applicable)

e)	Copy of Federal Permits (relevant federal permits including, but not limited to, Corp of Engineers 404 Dredge and Fill Permits)

f)	Copy of City of Overland Park Land Disturbance Permit

g)	Copy of adjacent cities Land Disturbance Permits (if applicable)

SECTION 3

Attach following drawings to this section:

a)	Vicinity Map - an area map showing the outline of the construction site and the general topographic features of the area at least one mile beyond the project site boundary

b)	Erosion and Sediment Control Plan Sheets, Detail Sheets and Drainage Area Map

c)	Erosion and Sediment Control Specifications included in the contract documents.

d)	Site Map - A copy of the ESC Plan Sheets may be used as the starting point for the site map.  This map  is a working document that summarizes the implementation of BMPs  throughout project construction, including:

	Erosion control measures (seeding, sodding, stockpile locations & protection, etc.)

	Sediment control measures (inlet protection, perimeter protection, sediment basins, construction entrances ,temporary crossings, etc)

	Location of chemical and waste controls (i.e. waste disposal, sanitary waste, concrete washouts and hazardous materials).

SECTION 4

Insert the following forms in this section:

	Stormwater Pollution Prevention Plan (SWPPP) Construction/Implementation Checklist

	Contractor Certification Form - This form is to be completed by each Contractor responsible for installation, operation, or maintenance of any construction stormwater best management practices (BMPs) necessary to complete the requirements of the Stormwater Pollution Prevention Plan. This completed form must be included in, or kept with, the Stormwater Pollution Prevention Plan for the project. The form can be found at:  http://www.kdheks.gov/stormwater/download/Contractor_Certification_Form.pdf

	Contractor’s Approved Project Schedule

	Potential Construction Site Stormwater Pollutants

	Initial Inspection Report – Initial inspections will be conducted by the City Construction inspector prior to land disturbance and after initial controls are installed.

	Regular Inspection Report Forms – The Contractor is responsible for conducting weekly and after rain inspections and correcting deficiencies.

	BMP Checklist – The BMP checklist should be used when conducting regular inspections.

	Quality Assurance Inspection Forms – The City Construction Inspectors will conduct quality assurance inspections that include reviewing the Contractor’s weekly inspections, following-up on deficiencies noted in regular inspections and assessing the effectiveness of the erosion and sediment control efforts. Quality assurance reviews will be conducted on a monthly basis; additional reviews will occur during a sequence change and if there are other special circumstances that warrant an inspection.

	Final Inspection Form – The final inspection will be conducted by the City Construction inspector after the site is substantially stabilized.

	Notice of Termination - Submission of the Notice of Termination (NOT) constitutes notice that the party relinquishes authorization for coverage under the Kansas Water Pollution Control general permit, or KDHE authorized successor permits, issued for discharge of Stormwater Runoff from Construction for the construction activity at the site named herein. Completion of the NOT does not automatically relieve the former permittee of any civil, criminal and/or administrative penalties. The form can be found at: http://www.kdheks.gov/stormwater/download/Notice_of_Termination.pdf

Optional Forms:

	SWPPP Modification Report Form – the modification form can be used to document any changes to the SWPPP by the project team.

	Amendment Log/Modification Report Form – The amendment log and modification form can be used to record major and minor modifications/amendments.

	Project Rainfall Log Form – The rainfall log can be used to record rainfall amounts or the project team can sign-up for email Erosion Control Alerts through Stormwatch visit,  http://www.stormwatch.com/weather/erosionControl.asp.

| Stormwater Pollution Prevention Plan (SWPPP) Construction/Implementation Checklist |
| --- |
| □ | Retain a copy of the SWPPP onsite |
| □ | Make SWPPP available upon request |
| □ | Signed certification forms in SWPPP |
| □ | Identify and record all potential sources of pollution to include: porta-pottys, fuel tanks, staging areas, waste containers, chemical storage areas, concrete cure, paints, solvents |
| □ | Describe what kind of construction or waste materials are expected to be stored on-site with updates recorded. Ex. Controls used to reduce pollutants from these materials |
| □ | Identify all operators for the project site and the areas of the site over which each operator has control. |
| Maintain Records of Construction Activities, including: |
| □ | Dates when major grading activities occur |
| □ | Dates when construction activities permanently cease on a portion of the site |
| □ | Dates of rainfall and the amount of rainfall |
| □ | Dates and descriptions of the character and amount of any spills of hazardous materials |
| □ | Records of reports filed with regulatory agencies if reportable quantities of hazardous materials spilled |
| Prepare Inspection Reports summarizing: |
| □ | Name of inspector |
| □ | Qualifications of inspector |
| □ | Measures/areas inspected |
| □ | Observed conditions |
| □ | Update or modify SWPPP to reflect changes at a site that effect discharge, or where inspections identify SWPPP/BMPs as ineffective |
| □ | Update SWPPP regarding modifications to BMPs within 7 days of such inspection |
| □ | Retain copies of inspection reports for 3 years from the date permit coverage is terminated |
| Report Releases of Reportable Quantities of Oil or Hazardous Materials within 24-hours of their occurrence: |
| □ | Notify National Response Center (800) 424-8802 |
| □ | Notify the Kansas Department of Health and Environment: 24-hour Spill Response (785) 296-1679; and Northeast District, Lawrence (785) 842-4600 |
| □ | Spills that pose immediate threat to public safety shall be reported immediately to: ▪ Overland Park Fire Department at 911 ▪ Kansas Division of Emergency Management (800) 275-0297 or (785) 296-8013 |
| □ | Modify the pollution prevention plan to include date of release, circumstances leading to the release and steps taken to prevent reoccurrence of the release |
| Modify Pollution Prevention Plan as necessary to: |
| □ | Comply with the minimum permit requirements when notified by U.S. Environmental Protection Agency or Kansas Dept. of Health and Environment that the plan does not comply |
| □ | Address a change in design, construction operation, or maintenance, which has an effect on the potential for discharge of pollutants |
| □ | Prevent reoccurrence of reportable quantity releases of a hazardous material or oil |

Potential Construction Site Stormwater Pollutants

(Indicate pollutants as appropriate)

|  | Trade Name Material | Chemical/Physical Description(1) | Storm Water Pollutants(1) |
| --- | --- | --- | --- |
| □ | Pesticides (insecticides, fungicides, herbicides, rodenticides) | Various colored to colorless liquid, powder, pellets, or grains | Chlorinated hydrocarbons, organophosphates, carbamates, arsenic |
| □ | Fertilizer | Liquid or solid grains | Nitrogen, phosphorous |
| □ | Plaster | White granules or powder | Calcium sulphate, calcium carbonate, sulfuric acid |
| □ | Cleaning solvents | Colorless, blue, or yellow-green liquid | Perchloroethylene, methylene chloride, trichloroethylene, petroleum distillates |
| □ | Asphalt | Black solid | Oil, petroleum distillates |
| □ | Concrete | White solid | Limestone, sand |
| □ | Glue, adhesives | White or yellow liquid | Polymers, epoxies |
| □ | Paints | Various colored liquid | Metal oxides, Stoddard solvent, talc, calcium carbonate, arsenic |
| □ | Curing compounds | Creamy white liquid | Naphtha |
| □ | Wastewater from construction equipment washing | Water | Soil, oil & grease, solids |
| □ | Sanitary wastes/sewage | Water, fecal matter | Bacteria, ammonia, nutrients |
| □ | Wood preservatives | Clear amber or dark brown liquid | Stoddard solvent, petroleum distillates, arsenic, copper, chromium |
| □ | Hydraulic oil/fluids | Brown oily petroleum hydrocarbon | Mineral oil |
| □ | Gasoline | Colorless, pale brown or pink petroleum hydrocarbon | Benzene, ethyl benzene, toluene, xylene, MTBE |
| □ | Diesel fuel | Clear, blue-green to yellow liquid | Petroleum distillate, oil & grease, naphthalene, xylenes |
| □ | Kerosene | Pale yellow liquid petroleum hydrocarbon | Coal oil, petroleum distillates |
| □ | Antifreeze/coolant | Clear green/yellow liquid | Ethylene glycol, propylene glycol, heavy metals (copper, lead, zinc) |
| □ | Erosion | Solid Particles | Soil, sediment |

(1)Data obtained from MSDSs when available

Initial Inspection of Erosion and Sediment Control

Project/LDP Number:   ______________________     Date:_____________________________

Contractor/Representative:____________________

Evaluated by Construction Inspector:____________________

A. Project Overview

	How Many Acres Total Does the Project Disturb? _________

	Project Start Date:_________   Project End Date:__________

	Phase I start date?_________

B. Paperwork

	*Does the project have a Land Disturbance Permit?	Yes	No        N/A

	*Is the SWPPP Notebook onsite? 	Yes	No        N/A

C. Site Preparation

	*Has the contractor installed temporary construction

entrance(s) and are the vehicles using it?	Yes 	No        N/A

	*Is there a place for concrete wash-out, is it clearly marked

and do concrete trucks appear to be using it? 	Yes 	No   	N/A

	*Is the site largely free of construction trash? 	Yes 	No        N/A                                   (cups, lunch sacks, material packaging, etc.)

	*Have perimeter sediment controls been installed?                       Yes 	No        N/A

	*Have pre-construction controls been installed per the plan         Yes 	No        N/A

been installed?

	*Have easily recognizable indications of the construction limits   Yes 	No        N/A

been installed? (fencing, staking, physical barriers)

* Must be “yes” or N/A in order for inspection to be “satisfactory”.

D. Approval

City staff  initial for approval:

_________Land disturbance work will proceed, as this site has met all the initial standard requirements of the City of Overland Park Erosion and Sediment Control measures.

_________Land disturbance work will not proceed as this site has not met all the initial standard requirements of the City of Overland Park Erosion and Sediment Control measures. The deficiencies below must be corrected in order to have a satisfactory inspection:

1.___________________________________________________________________2.___________________________________________________________________3.___________________________________________________________________4.___________________________________________________________________5.___________________________________________________________________

| Erosion and Sediment Control Inspection Report Form |
| --- |
| Project Name and Location |
| Weather: | Pollution Control Measures (BMP) Checklist: ____ Inlet Barrier (ie: gravel bags) ____ Sediment Barriers (ie: ditch checks) ____ Erosion Blankets, Hydromulch / Seed, etc ____ Stabilized Construction Entrance ____ Stream Crossings ____ Seed / Sod Areas ____ Sediment Basins & Discharge Locations ____ Borrow Areas ____ General Site Condition (trash, etc) |
| Rain in last 24 hrs (inches): |  |
| Owner / Permittee: |  |
| A. Current Construction / Active Areas: |  |
| B. Problem Areas / Special Observations(*Note problem areas ONLY below*): |
| BMP | Location | Observations, Effectiveness, & Corrective Actions Ordered |
| C. Listing of Areas where construction operations have permanently or temporarily stopped; stabilization measures initiated. |
| D. Have items noted on last inspection been corrected? Yes No ( if No, Explain:) |
| Note: Inspection comments above indicate deficiencies only. Deficiencies must be corrected within 7 days, unless otherwise noted. All other BMP’s on site are considered to be in good working condition. |
| Date of Inspection |  |  |  | Inspector Signature |
| 6 Goals ? No Sediment Leaves the Site ? Lines of Defense Everywhere & Always ? Cover Quickly |
| ? Protect the Swale, Ditch ,and Channel ? Keep Clean Water Clean ? Inspect, Clean & Fix |

| BMP INSPECTION CHECKLIST |
| --- |
| General notes about Inspections: 1) Site inspected weekly 2) Within 24 hours of the end of a storm with rain >0.5” 3) Deficiencies corrected within 7 calendar days of inspection | Key elements to look at during inspection 1) Proper installation 2) Operation 3) Maintenance |
| Inlet Barriers (ie:sand bags, gutter buddies, straw wattles) |
| v Is the structure deteriorating |
| v Is sediment >1/2 the height of structure? |
| v Evidence of water/sediment getting around or under barrier? |
| v Are there other structures that require inlet barriers? |
| Sediment Barriers (ie:ditch checks) |
| v Are they trenched in or falling down? |
| v Evidence of sediment/water getting around or under barrier? |
| v Is sediment more than 1/2 height of structure? |
| v Are there areas where more sediment barriers are required or need extended? |
| Perimeter Control (ie: silt fence, straw wattles) |
| v Is all the off-site water being diverted where applicable? |
| v Evidence of water/sediment getting around or under barrier? |
| v Are there areas that need extended or additions to other locations? |
| Stabilized Construction Entrance |
| v Is gravel clean or getting filled with mud? |
| v Evidence of sediment being tracked off site onto public streets? |
| Stream Crossing |
| v Is crushed stone in place? |
| v Wash outs? |
| Final or temporary Stabilization area |
| v Mulches/Grasses-are areas thinning or have been disturbed? Re-application required? |
| v Straw Blankets-are they deteriorating and need replaced? |
| Borrow Areas |
| v When on site or offsite borrow areas, which include contractor furnished, are to be excavated below ground elevations, an earth berm must be constructed around the borrow area to prevent runoff from entering excavation area |
| Sediment Basin |
| v Note the basin depth. Is the basin more than ½ full of sediment from original design? |
| v Condition of basin side slopes |
| v Evidence of overtopping embankment |
| v Condition of outfall |
| General Site Conditions |
| v Trash barrels-any evidence of trash lying around site |
| v Location of porta potties |
| v Leaking vehicles |
| v Concrete Washouts Designated |

Public Works Quality Assurance Field Review

Erosion and Sediment Control

Project/LDP Number: ___________________ Contractor/Representative:___________________

Date:_______________________  Evaluated by Construction Inspector:____________________

A.  Project Status: (brief description of the current phase of construction; major items of work in progress; and general observations of effectiveness and maintenance of site controls, and stormwater discharge at outfalls).

B. Deficiencies Noted (List any specific deficiencies found during the review).

C.  Have weekly and rainfall-required inspections been conducted by the Contractor since the last compliance evaluation? Were noted deficiencies corrected within 7 days?

Notice to Contractor:  All deficiencies must be corrected within 7 days unless otherwise noted.   A record of corrected deficiencies must be maintained.

Final Inspection of Erosion and Sediment Control

Project/LDP Number:   ________________________   Date:_____________________

Contractor/Representative:____________________________

Evaluated by Construction Inspector:____________________

Project Overview

	How Many Acres Total Does the Project Disturb? _________

	Project Start Date__________   Project End Date _________

Paperwork

	Is the SWPPP Notebook onsite? 	Yes	No        N/A

	Has a copy of the SWPPP been given to City staff	Yes	No

Final Site Preparation*

	Has the concrete wash-out area been cleaned? 	Yes 	No   	N/A

	Is the site free of construction trash? 	Yes 	No        N/A                                   (cups, lunch sacks, material packaging, wood debris, etc.)

	Have perimeter sediment controls been taken down?                    Yes 	No        N/A

	Have indications of the construction limits                                    Yes 	No        N/A

been taken down? (fencing, staking, physical barriers)

	Has all the dirt on the site been covered?                                       Yes 	No        N/A

	Have appropriate grasses/sod/trees been planted?                         Yes 	No        N/A

	Have the plants accepted?	Yes 	No        N/A

	Have gutters and streets been cleaned of soil/trash?                       Yes 	No        N/A

	Have all erosion controls been removed?                                       Yes 	No        N/A

* Must be “yes” or N/A in order for inspection to be “satisfactory”.

Approval

City staff initial for approval:

_________A Compliance certificate will be submitted, as this site has met all the requirements of the City of Overland Park Erosion and Sediment Control standards.

_________A Compliance certificate will not submitted until all above requirements of the City of Overland Park Erosion and Sediment Control standards have been met. The items below must be completed in order to have a satisfactory inspection:

1._____________________________________________________________

2._____________________________________________________________

3._____________________________________________________________

4._____________________________________________________________

| AMENDMENT LOG |
| --- |
| Project/LDP Number: _________________________________________ Contractor/Representative:_____________________________________ |
| Amend. No. | Date | Approved By | Describe Amendment in General (More details may be marked in the site map or noted in the daily inspection report) |

Optonal Form for Amendment Log- Use for major modifications that need approval, use site map or current amendment log for minor modifications.

SWPPP MODIFICATION REPORT FORM

Date Submitted: _________________________________________

Project/LDP Number: _________________________________________

Contractor/Representative:_____________________________________

| Submit To: | S-1 CITY City Engineer |  |
| --- | --- | --- |
| Address: |  |  |  |
| Telephone: |  |  |  |
| Facsimile: |  |  |  |
| Sent Via: | Facsimile | Courier | US Mail |

Authorized Author:						  Title:

Company:							  Project Role:

Signature:							  Date:

Modifications Required to the STORMWATER POLLUTION PREVENTION PLAN:

Reasons for Modifications:

| PROJECT NAME Project Owner Site Address City, State Zip Code | STORMWATER POLLUTION PREVENTION PLAN |  |
| --- | --- | --- |
|  | PROJECT RAINFALL LOG FORM |  |
| Day | YEAR: 20_____ |
|  | Jan | Feb | Mar | Apr | May | June | July | Aug | Sept | Oct | Nov | Dec |
| 1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 |  |  |  |  |  |  |  |  |  |  |  |  |
| 15 |  |  |  |  |  |  |  |  |  |  |  |  |
| 16 |  |  |  |  |  |  |  |  |  |  |  |  |
| 17 |  |  |  |  |  |  |  |  |  |  |  |  |
| 18 |  |  |  |  |  |  |  |  |  |  |  |  |
| 19 |  |  |  |  |  |  |  |  |  |  |  |  |
| 25 |  |  |  |  |  |  |  |  |  |  |  |  |
| 26 |  |  |  |  |  |  |  |  |  |  |  |  |
| 27 |  |  |  |  |  |  |  |  |  |  |  |  |
| 28 |  |  |  |  |  |  |  |  |  |  |  |  |
| 29 |  |  |  |  |  |  |  |  |  |  |  |  |
| 30 |  |  |  |  |  |  |  |  |  |  |  |  |
| 31 |  |  |  |  |  |  |  |  |  |  |  |  |
| totals |  |  |  |  |  |  |  |  |  |  |  |  |