Exhibit A

SCOPE OF Engineering Services for

137th Street & Metcalf Avenue Traffic Signal INSTALLATION (ts-0991)

and

138th Street & Metcalf Avenue Traffic Signal INSTALLATION (TS-0992)

SCOPE OF SERVICES

Consulting Engineer Responsibilities

Scope of project:  This project includes design, plans, and specifications for construction of traffic signal improvements at 137th Street and Metcalf Avenue and 138th Street and Metcalf Avenue.

# Task I.	Data Collection

# Field Survey

## 1.01 	Field Survey

### A.	Complete field survey as required to pick up additional utilities.

### B.     Additional survey is required for the west leg of 137th Street including spot checks on the ADA ramps located on the wet leg to verify that they conform to current design standards.

### C.    Additional survey may be required for the west leg of 138th Street or coordination with the appropriate design consultant.

## 1.02 	Survey Basemap

### A.	Complete conversion of field survey completed to basemap.

# Task II.	Preliminary Design

## 1.01 	Data Collection

### A.	Attend pre-design meeting.

### B.	Develop design criteria for the project; prepare design memorandum.

### C.	Develop detailed design schedule including the following due dates:

### 1.	Notice to Proceed

### 2.	Preliminary plans due

### 3.	City Review Complete

4.	90% Plans Due

5.	City Review Complete

6.	Final Plans Due

### D.	Field data collection

#### 1.	Field surveys (spot-checks of information provided by the City, including lane widths, sidewalk locations, existing pavement markings, and box locations in areas near future poles). Review the condition and location of existing signal poles and service boxes. The City shall provide the bolt pattern for the mast-arm connection located on the existing signals posts located in the median on Metcalf Avenue.

#### 2.	Contact utility companies or one call center as appropriate for field marking of utility locations.

### E.	Coordinate power location with Kansas City Power & Light Company.  Copy the City of Overland Park with all correspondence to KCP&L.

### F.	Obtain from the City current daily traffic volumes and peak period turning movement counts.

### G.	Determine the required lane configurations, signal phasing, and traffic control for the project.  Examine the existing lane geometrics along the project and determine traffic control and/or geometric improvement recommendations as might be warranted.  (No level of service analysis is included.)  Meet with the City to review the recommendations.

### H.	Coordinate design of the traffic signals with the existing and proposed development in the surrounding area.

## 1.02	Prepare base map at a scale of 1 inch = 20 feet.

## 1.03	Develop preliminary plans (standard details and sheet elements will be provided electronically by the City):

### A.	Cover sheet

### B.	Plan sheets:

### 1.	Traffic signal layout including location of all proposed poles, loop detectors and detection zones, service, junction and fiber optic boxes, and the signal controller.

### 2. 	Proposed signal phasing.

### 3. 	All wiring details and diagrams.

### C.	Quantity sheets

### D.	Detail sheets (using standard details provided by the City).

### E.	Intersection lighting design – incorporation of intersection lighting onto traffic signal poles.  (No detailed lighting analysis is included.)

### F.	Preliminary traffic control (using standard details provided by the City).

### G.	Preliminary pavement marking and signing.

### Prepare detailed wheelchair ramp design layout sheets.

1.	Consultant shall assume that the ADA ramps recently constructed with Truncated domes on the east side of Metcalf Avenue at 137th and 138th Street meet current standards and do not need to be modified. Also assume that the design of the wheelchair ramps for the west leg of 138th Street will be completed with the development located west of Metcalf Avenue. The consultant shall verify that the existing wheelchair ramps on the west leg of 137th Street meet current design standards and upgrade to such as required. If the current grades for the ramps are adequate then only truncated domes “adhesive type” will be added to the current ramps.

### I.	Right-of-way as provided by the City.  Any easements required for this project will be acquired by the City.  (Any needed legal descriptions would require a supplemental agreement.)

### J.	Preliminary cost estimate shall be furnished based on the experience and qualifications of the consulting engineer/architect’s best judgment as an experienced and qualified design professional, familiar with the construction industry and advice the City of, in its opinion, the amount budgeted for construction is not sufficient to adequately design and construct the improvement as requested.

## 1.04	Submit three full-size sets of preliminary plans to City for review.

## 1.05	Meet with City at the time of delivery of preliminary plans.

## 1.06	Field Check to be performed with representatives of the Consulting Engineer and the City at the project site with appropriate detailed plans.

# Task III.	Final Design

## 2.01	Prepare detailed plans and specifications.

### A.	Cover sheet.

### B.	Plan sheets.

### C.	Quantity sheets.

### D.	Detail sheets.

### E.	Pavement marking and signing (with detail sheets provided by the City).

### F.	Intersection lighting.

### G.	Detailed wheelchair ramp design layout sheets.

### H.	Existing and proposed right-of-way (as known from existing plans).

### I.	Traffic control detail sheets.

### J.	Location of known existing utilities and underground facilities.

### K.	Location of existing utilities and underground facilities.

### L.	Fiber Interconnect design shall include connecting to the current conduit and fiber that runs North and South on the East side of Metcalf Avenue. Consultant shall run a 6 fiber from the signal controller to the existing fiber and coordinate the splice diagram with the City for connecting the 6 fiber to the existing 72 fiber.

## 2.02	Preparation of Bid Documents will be performed by the City.

## 2.03	Prepare a detailed opinion of probable cost (including appropriate contingency).

## 2.04	Prepare 90% plans and cost opinion to City for review.

## 2.05	Upon receipt of City comments on 90% submittal, make necessary modifications and furnish five sealed copies of final plans and specifications.

### A.	Plan sets will be provided as follows:

#### 1.	Full size (22” X 34”) – three sets

#### 2.	Half size (11” X 17”) – two sets

### B.	These plans are to be provided at no additional cost, and are separate from those sold to prospective bidders.

## 2.06	At the completion of the project, furnish to the City a CD containing CAD drawings of the project in the Consulting Engineer’s digital format (ACAD version 14 for Windows) and TIFF images in compressed CCITT, group 4 at 200 dpi format for the City’s future use.  The record contract documents for the project will be the original sealed drawings.

## 2.07	Submit one full size set (bound) and one CD of final plans to each of the City of Overland Park plan holders (eight plan holder’s total).

## 2.08	Meet with the City at the time of completion of final plans.

# Task IV.	Bidding

## 3.01	Prepare and provide plans and specifications to bidders at cost to recover expenses of duplication and handling.

## 3.02	Prepare written addenda to the bidding documents as required and or requested.

# Task V.	Construction Services

## 4.01	Be available for discussion and consultation during the construction phase.  Construction observation will be the responsibility of the City.

## 4.02	Prepare plan revisions as necessitated by conditions encountered in the field during construction, with the exception of traffic control plans.

## 4.03	The City will review all catalog cuts and shop drawings for general conformity to the plans and contract documents.

## 4.04	Prepare final record drawings which reflect:

### A.	All change orders.

### B.	Minor design changes.

### C.	Changes made in the field by City representatives that are marked on the plan set.

### D.	Submit updated CAD drawings and TIFF images and three full size paper copies of the revised sheets.

City Responsibilities

1.	The City shall provide existing traffic data at each intersection.

2.	The City shall provide record drawings of each intersection, if available.

COMPLETION TIME

The Consulting Engineer hereby agrees to complete the plans in accordance with the attached schedule.