City of Overland Park

Bridge Design Information

## Hydraulic Design

- Non RCB bridges shall pass the 100-yr event with 2.0 ft desirable free board, 1.0 ft minimum.

- RCB's shall meet the roadway overtopping criteria as set forth in the OPMC.

- FEMA no-rise criteria shall also be met when in a FEMA defined floodway.

## Utilities

- Requests to place conduit in new slab bridges will be considered if the utility is willing to pay for the conduit construction.

- Utilities will not be allowed to attach to existing bridges.

## Bridge typical section

- Sidewalks shall be in the same plane and have the same cross-slope as the bridge deck.

- Silica fume overlays will not be used on bridge decks. Decks shall be constructed in a single pour, using concrete as per the Overland Park specifications.

- Rebar clearance shall be 3" for top deck reinforcement.

## Bridge railing

- Use corral rail w/o curb unless crossing over another roadway.

- Galvanized steel railing shall be used on Pedestrian/bike sidewalks (see Lamar over Indian Creek, BR-0005).

- A galvanized steel railing is required on top of corral rail separating the roadway from a bike path. The overall height of the corral/steel railing shall match the height of the exterior railing.

- No railing is required above the corral rail separating the roadway from a pedestrian-only sidewalk.

## Approach slab

- Follow KDOT standards.

- The need for approach guardrail is based on clear zone criteria.

- On low speed roads, taper corral rail from full height down to the curb.

- If guardrail is warranted, begin standard flared guardrail at end of corral rail.

- Flared guardrail and sidewalk should fit within r/w limits. Attenuators may be used if flared guardrail cannot be used.

## Drilled shafts

- Drilled shaft foundations require specialized inspection. If drilled shaft foundations are specified on the plans, a geotechnical firm should be hired to perform the inspection as per KDOT.

## Box Culverts

- Use standard KDOT design for RCB’s.

- Wingwalls shall be detailed with a vertical joint to separate them from the RCB.

- Footings for the wingwalls shall be set below the frost line.