# City of Overland Park

# Public Works Department

# Traffic Services Division

# Approved Materials List

Table of Contents

## Fiber Optic Approved Materials List

ITS Approved Materials List

#### Pavement Marking Approved Materials List

Signing Approved Materials List

Specialty Items Approved Materials List

## Street Lighting Approved Materials List

## Traffic Control Approved Materials List

#### Traffic Signal Approved Materials List

NOTE:	This document is provided as a benefit to contractors and suppliers who are bidding projects for the City of Overland Park.  Only products identified on this list will be approved for installation on City construction projects.  This list shall not be used as a substitute for catalog cuts or material approval.  All material approvals shall be submitted on the approved City of Overland Park Contract Project Submittal form.  The form is available at City Hall by contacting Bruce Wacker at (913) 895-6027.  Failure to comply will be cause for rejection of materials until proper submittals are received.  This list is updated periodically.  The contractor or supplier shall contact the City of Overland Park to make sure that they have the most current list prior to bidding a project.  Failure to do so shall not constitute a legitimate claim for change orders.

# Fiber Optic System Approved Materials List

| Cables | Locating Materials | Splice Enclosures |  |
| --- | --- | --- | --- |
| Conduit and Couplings | Encoders | Termination Drop Cables |  |
| Ethernet Switches | Service Boxes | Terminal Servers |  |

### Cables					Back to Fiber Optic System Table of Contents					Back to Main

| Fiber Optic Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Alcoa AFL Telecommunications | LE1449CC101N1 – 144 Count LE0729C6101N1 – 72 Count LE0369C5101N1 – 36 Count LE0129C5101N1 – 12 Count LE0069C5101N1 – 6 Count | 7/27/04 | Single Mode Fiber Non-Armored Loose Tube Cable |
|  | Chromatic Technologies | D740L12-144-010X – 144 Count D740L12-72-010X – 72 Count D740L6-36-010X – 36 Count D740L6-12-010X – 12 Count D740L6-06-010X – 6 Count | 10/21/02 |  |
|  | Corning Cable Systems | ALTOS All-Dielectric Gel-Free Cables 144EW4-T4101D20 – 144 Count 072EW4-T4101D20 – 72 Count 036EW4-T4101D20 – 36 Count 012EW4-T4101D20 – 12 Count | 7/2/07 |  |
|  | Draka Comteq | F-ETH1JKT-12-ES-144-E3 – 144 Ct F-ETH1JKT-12-ES-072-E3 – 72 Ct F-ETH1JKT-12-ES-036-E3 – 36 Ct F-ETH1JKT-12-ES-012-E3 – 12 Ct | 8/24/11 |  |
|  | Mohawk | M9X509 – 144 Count M9X507 – 72 Count M9X502 – 36 Count M9X511 – 12 Count M9X510 – 6 Count | 11/3/05 |  |
|  | Superior Essex | 111443101 – 144 Count 110723101 – 72 Count 110363T01 – 36 Count 110123T01 – 12 Count 110063101 – 6 Count | 4/22/05 |  |

| Fiber Optic Plenum Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Chromatic Technologies | 800T12-144-010X – 144 Count 800T12-72-010X – 72 Count 800T6-36-010X – 36 Count 800S-06-010X – 6 Count | 10/21/02 | Single Mode Fiber |

| Fiber Optic Riser Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Chromatic Technologies | 400T12-72-010X – 72 Count | 10/21/02 | Single Mode Fiber |

| Fiber Optic Patch Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | ICC | ICFOJ3M302 | 7/15/08 | ST-LC connectors, 6’ duplex, single mode |
|  | Major Custom Cables | FXDSLCST-XM | 8/7/09 |  |
|  | Quiktron | 810-L27-LLL V-Series 2F LC-ST (Drawing D100855) | 8/5/10 |  |

| #10 AWG System Tracer Wire | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cerowire Wire & Cable Co., Inc. | UL file # E15119 | 5/5/03 | Red Insulation, Stranded copper #10 AWG THHN 600 volt |
|  | Encore Wire LTD | UL file # E123774 | 8/1/03 |  |
|  | Essex Group, Inc. | Product Number 070101 UL File # E14656 | 2/1/01 |  |
| CLOSED 9/03 | Rome | 2020 UL file #13662 | 5/5/03 |  |
|  | Senator / Southwire | Red – 22-97-57 UL file # E23919 | 5/5/03 |  |
|  | Service Wire | UL file # E105667 | 5/7/02 |  |

### Conduit and Couplings			Back to Fiber Optic System Table of Contents					Back to Main

| HDPE Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Dura-Line now owns Arnco, Boreflex, Carlon and Lamson Pipe | Dura-Line | 3” – SW 400 300 N033 2” – SW 400 200 N033 | 8/2/01 | 2” or 3” Schedule 40 as indicated in plans Orange color Smooth solid wall UV Stabilized |

| HDPE Couplings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | American Polywater | Bonduit Conduit Adhesive Use only with Cantex Sch 40 PVC Longline Coupling: 2” – 6202000 3” - 6202005 | 10/11/10 |  |
|  | Cabletec | 2” – AS 2.375 3” – AS 3.500 | 8/2/01 |  |
|  | Central Plastics Company | Electrofusion Couplings 2” IPS 575-0042 3” IPS 575-0043 | 5/5/06 |  |
|  | Dura-Line | PushLock Couplings 2” – 1-908353 | 10/5/10 |  |
|  | Tyco Electronics / Jackmoon | Moon-Link Transparent Duct Coupling 2” – 20TC238SP 3” – 30TC350SP | 12/23/02 |  |
|  | Unitex | Pro-Poly CA Adhesive Use only with Cantex Sch 40 PVC Longline Coupling: 2” – 6202000 3” - 6202005 | 1/9/06 |  |

| Expansion Couplings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cantex | 1” – 5144033 1 ½” – 5144035 2” – 5144036 3” – 5144038 4” – 5144040 | 5/5/03 |  |
| Formerly Carlon | Thomas & Betts | 1” – E945F 1 ½” – E945H 2” – E945J 3” – E945L 4” – E945N | 5/26/09 |  |

| Repair Couplings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Formerly Carlon | Thomas & Betts | Split Duct Coupling 2” – 49011SD-010 3” – 49013SD-010 4” – 49015SD-010 | 5/26/09 | Used to repair damaged fiber optic conduit when not feasible to remove fiber cable and re-splice |

### Ethernet Switches			Back to Fiber Optic System Table of Contents					Back to Main

| Ethernet Switch | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cisco Systems, Inc | Catalyst WS-C2955S-12 AC Power Converter PWR-AC-2955 19” Rack Mount Kit - STK-RACKMNT-2955 Patch Cables (ST-LC connectors) | 5/7/08 | Hardened Ethernet Switch w/ DIN Rail Adapter 12 10/100 Ports AC Power Converter 19” Rack Mount Kit Two, 6’ Long Duplex Single Mode Fiber patch cables (ST-LC connectors) |

### Locating Materials			Back to Fiber Optic System Table of Contents					Back to Main

| Tracer Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cerro Wire & Cable Co, Inc. | Red – 112-3803 UL file # E15119 | 5/5/03 | Stranded copper THHN/THWN #10 AWG |
|  | Encore Wire LTD | UL file # E123774 | 8/1/03 |  |
| Purchased by Southwire Co. | Essex | Product Number 070061 UL file # E14656 | 8/21/03 |  |
|  | Rome Cable Corp | 2020 UL file # E13662 | 5/5/03 |  |
|  | Senator / Southwire | Red – 22-97-57 UL file # E23919 | 5/5/03 |  |
|  | Service Wire Co | UL file # E105667 | 5/7/02 |  |
|  | United Copper Industries | Red – 325372 (500’ reel) Red – 325574 (2,500’ reel) UL file # E194031-A | 5/26/09 |  |

| Ground Rods | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Chance/Hubbell | Cat. No. C611380 | 4/24/12 | ½” x 8’-0” long Copper clad steel core UL listed |
|  | Erico Inc. / Eritech | Cat. No. 611380 | 2/27/02 |  |
|  | ITTBlackburn | Cat. No. 5008 | 5/5/03 |  |
|  | Josyln | Cat. No. J-8328 | 5/5/03 |  |

| Ground Rod Clamp | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Burndy | GRC 12 | 2/27/02 | Hex head set screw Copper alloy Long bearing surface UL listed |
|  | Erico Inc. / Eritech | Part No. HDC12 – ½” rod Part No. HDC34 – ¾” rod | 12/1/05 |  |
|  | ITT Blackburn | Type JAB-12H | 5/5/03 |  |

| Conduit Markers | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Carsonite | CBM206604 | 10/23/01 | 66” long x 2 ½” min wide Orange in color City provides identification stickers |

### Encoders					Back to Fiber Optic System Table of Contents					Back to Main

| Ethernet Video Encoders | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| For Maintenance Use Only | Verint Nextiva | S1970e-T-XT | 7/12/07 | Product has been Discontinued |

### Service Boxes				Back to Fiber Optic System Table of Contents					Back to Main

| Type I Fiber Optic Service Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001974TAPCX24 (24”x36”x24”) | 7/30/01 | Logo to read “Fiber Optics” Cover to be 3” thick Hex head bolts |
|  | Carson Industries | H2436-24 – Box only H2436-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-2436-24 – Box only SC30-2436-03 – Cover only SA33-2436-24 – Assembly | 8/8/03 |  |
|  | Highline | PHB243624 – Box only CHC2436HF – Cover only PHA2436HF2 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 243624PCB – Box only 2436PCC – Cover only 243624PC - Assembly | 10/17/11 |  |
|  | New Basis | PCB243624A04 – Box only PCC243605A04 – Cover only | 2/26/02 |  |
|  | Quazite | PG2436BA24 – Box only PG2436CA0021 – Cover only | 5/05/03 |  |

| Type II Fiber Optic Service Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001430TAPCX24 (30”x 48”x 24”) | 7/30/01 | Logo to read “Fiber Optics” Cover to be 3” thick two-piece underlapping Hex head bolts |
|  | Carson Industries | H3048-24 – Box only H3048-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-3048-24W – Box only SC30-3048-23W – Cover only SA33-3048-24W – Assembly | 8/8/03 |  |
|  | Highline | PHB304824 – Box only CHC3048HF-2PC – Cover only PHA304824HF4 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 304824PCB – Box only 3048PCC – Cover only 304824PC - Assembly | 10/17/11 |  |
|  | New Basis | PCB304824A04 – Box only PCC304815A04 – Cover only | 2/26/02 |  |
|  | Quazite | PG3048BA24 – Box only PG3048CC0046 – Cover only | 5/5/03 |  |

### Splice Enclosures			Back to Fiber Optic System Table of Contents					Back to Main

| Splice Enclosures | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Corning Cable Systems | SCF-6C-XX-YY-Z – Single end cap XX = body length (22 = 22 inches or 28 = 28 inches) YY = fiber configuration (01=Full slack storage, 02=Reduced slack storage Z = splice tray configuration (blank = 0.2” tray height, F = 0.4” tray height) SCF-6T – Double end cap | 7/26/05 | Bell Type Enclosures |
|  | Tyco Electronics Corporation | FOSC 450 | 10/12/05 |  |
|  | Windsor Communications | 570-22-AD | 10/12/05 |  |

### Termination Drop Cables		Back to Fiber Optic System Table of Contents					Back to Main

| Patch ITS Drop Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Fiber Connections, Inc. | Gator Patch 6 Fiber – G320G006FRB-Length 12 Fiber – G620G012FRB-Length | 1/10/06 | 6 or 12-Fiber – Single mode 6 or 12 port rack mount for ST connectors |
|  | Major Custom Cable | Z-Stack 6 Fiber – FCZS6ASTUB 12 Fiber – FCZS12ASTUB | 3/23/09 |  |

### Terminal Servers				Back to Fiber Optic System Table of Contents					Back to Main

| Terminal Server | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Comtrol Network Enabling Devices | DeviceMaster RTS 1-Port Part Number 99000-0 | 9/1/05 | Single Port Supply with 6’ CAT 5e Network Patch Cable |

# ITS Approved Materials List

| Cable | Conduit | RWIS Equipment |  |
| --- | --- | --- | --- |
| CCTV Cameras | DMS Structures |  |  |
| CCTV Camera Mounting Bracket | Digital Message Signs |  |  |

### Cable						Back to ITS Table of Contents							Back to Main

| DMS Control Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Owned by Belden | Manhattan Wire Products / Belden | M3992 for RS-485 Cable | 11/15/05 | 24 AWG 4 pair communication cable shielded |

| DMS Power Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Southwire | UL E32071 S | 11/15/05 | Type USE-2 or RHH or RHW-2 600 Volt |

| RWIS RS-485 Data & Power Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | General Cable | PE-39 AL #7524507 | 11/15/11 | 19 AWG (6 pair) w/ drain wire with ETPR compound filling and aluminum corrugated shield |
|  | Superior Essex | PE-39 SEALPIC-F #04-026-21 | 1/24/12 |  |

### CCTV Cameras				Back to ITS Table of Contents							Back to Main

| CCTV Camera | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Axis Communications | Q6034-E with a T8124 1-port High PoE Midspan and 35899 RJ-45 Data Connector | 9/1/11 | High Definition IP PTZ Camera with Power over Ethernet injector module. See Traffic Signal Grounding Equipment for the RJ-45 Data Protector |

### CCTV Camera

### Mounting Brackets			Back to ITS Table of Contents							Back to Main

| CCTV Camera Mounting Bracket for Signal Pole | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Axis Communications | T91A67 Pole Mount | 9/1/11 |  |

### Conduit					Back to ITS Table of Contents							Back to Main

| Flexible Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| For DMS Signs | Electri-Flex Co. | Liquatite NM-13 | 11/15/05 | 1” Flexible Non-Metallic Liquid Tight Conduit |

### Digital Message Signs			Back to ITS Table of Contents							Back to Main

| Digital Message Signs | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Skyline Products, Inc. | VMSLED-L-3-08F-28x110-I | 4/26/05 |  |

### DMS Structures				Back to ITS Table of Contents							Back to Main

| DMS Structures | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Steve Johnson Companies | Job Number 7061* *Job number will change with every project #7061 135th St Widening/US 69 NB Ramp #8029 135th St Widening #8045 119th St Corridor #8588 Antioch Road 151st to 167th | 10/14/05 |  |

### RWIS Equipment			 	Back to ITS Table of Contents						Back to Main

| RWIS Equipment | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Made by Innovative Dynamics | High Sierra Electronics | 2020EW Remote Road Surface Condition Sensor – Model 5433-18 with Weather Shield Mini RWIS RPU – Model 5470-03 | 11/15/11 | The RPU includes: 1-Unit 19”x 8” Rack Enclosure Hammond RM1U1908VBK RWIS RS 485 Surge Protector – EDCO COHP-015 RWIS DC Power Suppressor – EDCO OPX-015 |

# Pavement Marking Approved Materials List

| Cold Plastic | Glass Beads | Preformed Thermoplastic | Urethane Acrylate |
| --- | --- | --- | --- |
| Epoxy Markings | Methyl Methacrylate Markings | Thermoplastic | Waterborne Paint |

### Cold Plastic				Back to Pavement Marking Table of Contents					Back to Main

| Temporary Cold Plastic Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | 3-M Company | Stamark Intersection Grade Tape A 420 – White SMS-L420-LA – Left Arrow SMS-L420-RA – Right Arrow SMS-L420-SA – Straight Arrow SMS-L420-ON – “ONLY” | 5/5/03 |  |

| Durable Pre-Formed, Patterned Cold Plastic | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | 3-M Company | Stamark Intersection Grade Tape A380I ES – White A381I ES - Yellow SMS-L380I ES-LA – Left Arrow SMS-L380I ES-RA – Right Arrow SMS-L380I ES-SA – Straight Arrow SMS-L380I ES-ON – “ONLY” | 5/7/08 |  |

### Epoxy Markings				Back to Pavement Marking Table of Contents					Back to Main

| Epoxy Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Poly-Carb, Inc. | MARK-55.2 Part A (White) MARK-55.2 Part A (Yellow) MARK-55.2 Part B | 2/6/06 |  |

### Glass Beads				Back to Pavement Marking Table of Contents					Back to Main

| Glass Beads | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Potters Industries | VISIBead | 5/5/03 | AASHTO M-247-81 Type 1 KS FP96T4 KS |
|  | Swarco |  |  |  |
|  | Swarco Reflex Inc. | Swarco Reflex Glass Beads (Type I KS) Megalux Glass Beads (FP96T4 KS) | 2/6/06 |  |

### Methyl Methacrylate Markings	Back to Pavement Marking Table of Contents					Back to Main

| Methyl Methacrylate Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Ennis Paint | Duraset 1/1P | 2/6/06 |  |

### Preformed Thermoplastic		Back to Pavement Marking Table of Contents					Back to Main

| Preformed Thermoplastic Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Purchased by Flint Trading as of 3/1/06 | Flint Trading / Formerly Zumar Industries, Inc. | Hot Tape 6” White Roll – HT895032 12” White Roll – HT895052 12” x 3’ White – HT894694 24” White Roll – HT895078 24” x 3’ White – HT894728 12” Yellow Roll – HT895054 12” x 3’ Yellow – HT894702 Left Arrow – HT894742 Right Arrow – HT894746 Straight Arrow – HT894898 Comb. Straight/Left Arrow – HT894748 Comb. Straight/Right Arrow –HT894752 ONLY Marking – HT894844 | 7/27/11 | 90 mil thickness |
|  | Swarco / Colorado Paint | 6” White Roll – 3506 12” White Roll – 3510 12” x 3’ White – 3482 24” White Roll – 3516 24” x 3’ White – 3488 12” Yellow Roll – 3511 12” x 3’ Yellow – 3489 Left Arrow – 3519 Right Arrow – 3520 Straight Arrow – 3524 Comb. Straight/Left Arrow – 3527 Comb. Straight/Right Arrow – 3528 Comb. Straight/Left/Right Arrow – 3529 ONLY Marking – 3615 Yield Marking – 12” x 18” – 3541 Yield Marking – 24” x 36” – 3543 48” x 48” Handicap Symbol White on Blue – 3802 | 3/9/12 |  |

### Thermoplastic				Back to Pavement Marking Table of Contents					Back to Main

| Thermoplastic Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Ennis Paint | Pavemark 884034 – White 884058 – Yellow 884490 – White 885035 – Yellow | 5/5/03 |  |
|  | Sherwin Williams / Dobco | W1X1656 – White Y1X1606 - Yellow | 12/15/10 |  |
|  | Swarco / Colorado Paint | 2633 – White 2897 – Yellow | 5/15/09 |  |

### Urethane Acrylate			Back to Pavement Marking Table of Contents					Back to Main

| Urethane Acrylate Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Swarco / Colorado Paint | MFUA-10 3186 – Yellow 3180 – White 3185 – Catalyst – Part B | 1/11/12 |  |

### Waterborne Paint				Back to Pavement Marking Table of Contents					Back to Main

| Waterborne Paint Markings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Sherwin Williams | 8000-03790 – White 8000-04665 – Yellow | 6/15/05 |  |
| For City Maintenance Operations | Diamond Vogel | UC-3588 – Yellow UC-1516 – White | 2/14//12 | 55 gallon drum Meets TT-P-1952 E |
| For City Maintenance Operations | Sherwin Williams | TM2153-27 – Yellow TM2152-27 – White | 2/14/12 |  |
| For City Maintenance Operations | Swarco / Colorado Paint | 1166 – Yellow 1160 – White | 3/9/12 |  |

# Signing Approved Materials List

| Aluminum Sign Blanks | Driver Feedback Signs | Posts | Sign Sheeting |
| --- | --- | --- | --- |
| Blank-Out Signs | Illuminated Street Name Signs | School Zone Flashers |  |
| Cable for Illuminated & Blankout Signs | Mounting Brackets |  |  |

### Aluminum Sign Blanks			Back to Permanent Signing Table of Contents					Back to Main

| Standard Signs | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hall Sign |  |  | 0.080” Thick 5052H38 or 6061-T6 aluminum alloy |
|  | Lyle Sign, Inc. |  |  |  |
|  | National Sign |  |  |  |
|  | Newman |  |  |  |
|  | The Work Zone, Inc. | 5052H38 aluminum |  |  |
|  | Vulcan Sign |  |  |  |

| Overhead Street Name Signs | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hall Sign |  |  | 0.125” Thick 5052H38 or 6061-T6 aluminum alloy |
|  | Lyle Sign, Inc. |  |  |  |
|  | National Sign |  |  |  |
|  | Newman |  |  |  |
|  | The Work Zone, Inc. | 5052H38 aluminum |  |  |
|  | Vulcan Sign |  |  |  |

### Blank-Out Signs				Back to Permanent Signing Table of Contents					Back to Main

| R10-11 “No Turn on Red” Ball symbol | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | M-Systems, Inc. | R10-11 | 1/12/09 | 30”x 36” Front Lens: Pebble Text with “Red Ball” symbol |

### Cable for Illuminated Street

### Name Signs & Blankout Signs	Back to Permanent Signing Table of Contents					Back to Main

| Sign Power Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Advanced Digital Cable | 8103 | 10/23/08 | 1-3c#14 AWG Stranded Copper IMSA 19-1 |
|  | Falcon Fine Wire | 980314X19-1 | 11/6/08 |  |

### Driver Feedback Signs			Back to Permanent Signing Table of Contents					Back to Main

| Sign Power Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | 3M | 75-0301-6563-5 – Urban Driver Feedback Sign (31” x 40”) 75-0301-6578-3 – DC Solar Kit 75-0301-6580-9 – DC Battery Charger Kit B | 5/1/09 |  |

### Illuminated Street Name Signs	Back to Permanent Signing Table of Contents					Back to Main

| Illuminated Street Name Signs | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Southern Manufacturing / Accord Industries | 619S-RM-TB: 6’ x 19” 819S-RM-TB: 8’ x 19” 624S-RM-TB: 6’x 24” 824S-RM-TB: 8’ x 24” | 10/29/08 | 120/240-volt self sensing power supply Translucent DG3 retroreflective sheeting Single sided face, rigid mount top and bottom Clearview Highway 5-W font |

### Mounting Brackets			Back to Permanent Signing Table of Contents					Back to Main

| Aluminum Sign Mast Arm Brackets | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AB0142-A-L Astro Sign-Brac | 5/18/05 | A = Sign Height minus 6” L = Cable Length |

| Illuminated Street Name Sign Brackets | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AB0125-L Astro Sign-Brac | 10/29/08 | L = Cable Length |

| Wing Mounting Brackets | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hall Signs | 16 ½” - #8 24” - #800 | 8/3/07 | A380 Alloy |
|  | Lyle Signs, Inc. | AL-13 | 8/3/07 |  |

| Round Pole Mounting Bracket | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Band-It | D02189 | 8/3/07 | 1-Bolt Flared Leg |
|  | Gerrard | ST021 | 8/3/07 |  |
|  | It Straps On, Inc. | SB021 | 8/3/07 |  |
|  | TAPCO, Inc. | 35-8 | 8/3/07 |  |

| Sign Banding | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Band-It | C20699 | 8/3/07 | Type 201 Stainless Steel 0.030” Thick ¾” Wide |
|  | Gerrard | ST206 | 8/3/07 |  |
|  | It Straps On, Inc. | BA206 | 8/3/07 |  |
|  | Panduit | MSW75T30-CR2 | 11/5/12 |  |
|  | TAPCO Inc. | 497-1 | 8/3/07 |  |

| Banding Buckle | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Band-It | C25699 | 8/3/07 | Type 201 Stainless Steel Buckle For 0.030” Thick x ¾” Wide Banding |
|  | Gerrard | ST256 | 8/3/07 |  |
|  | It Straps On, Inc. | BU256 | 8/3/07 |  |
|  | Panduit | MSBW75-C2 | 11/5/12 |  |
|  | TAPCO, Inc. | 497-2 | 8/3/07 |  |

### Posts						Back to Permanent Signing Table of Contents					Back to Main

| 1 ¾” x 1 ¾” Posts | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Unistrut Distribution Co./ Allied Mechanical Tube Division | Telespar Square Tubular Sign Supports – 16F12PXXPG | 8/31/12 | 12 Gauge Pre-punched holes on all sides Galvanized XX = Length (even 2’ increments up to 24’) |

| 2” x 2” Anchor | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Unistrut Distribution Co./ Allied Mechanical Tube Division | Telespar Square Tubular Sign Supports – 20F12A03PG | 11/9/12 | 12 Gauge Pre-punched holes on all sides Galvanized 36” length |

| 2 ¼” x 2 ¼” Sleeves | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Unistrut Distribution Co./ Allied Mechanical Tube Division | Telespar Square Tubular Sign Supports – 22F12APG | 8/31/12 | 12 Gauge Pre-punched holes on all sides Galvanized 18” length |

### School Zone Flashers		 	Back to Permanent Signing Table of Contents					Back to Main

| Master Radio Assembly | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | Master Radio Assembly – RTC#501676F Master Radio Only – RTC #300650A | 9/15/10 | Assembly installs in traffic signal cabinet and consists of: Ethernet LAN Assembly Serial Port Server, Power Supplies, Cables, 6dB Omni Antenna & 50ft Lead |

| Remote Radio | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | RTC #300600 | 9/15/10 | Installs at beacon assembly. |

| Surge Protector Polyphaser | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | #IS-50NX-C2 | 9/15/10 | Installs at traffic signal cabinet |

| Time Switch | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | RTC AP-22 #503644 | 9/15/10 | Installs at beacon assembly. Includes antenna and CPC Harness |

| Yellow Ball LED | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | DuraLED 433-3230-901XL | 4/30/10 | 12-volt power requirement |
|  | GelCore | DR6-YTFB-23B | 5/5/03 |  |

| Vehicular Signal Head | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Automatic Signal / Eagle Signal | SA101A1111YBB – 1 Section | 5/5/03 |  |

| Side-of-Pole Bracket | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Gades Sales | UKS-1452Y / PDM-405 | 5/5/03 |  |

| Solar Panel | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | Solar Panel | 5/5/03 | 80 Watt w/ mounting brackets |

| Solar Flasher Panel | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | 502598TFA | 5/5/03 | “L” Panel |

| Flasher | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | DC2F | 5/5/03 | 12-Volt, Solid State, w/ LED indicators DC 2-Circuit Flasher 8-Pin Octal Base |

| Solar Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | RTC Manufacturing, Inc. | RTC-503568 | 5/5/03 |  |

| Screw-In Foundation | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | JH Botts | JHB660914 | 5/5/03 | Shaft Diameter – 6” Shaft Length – 5’-0” Plate Size – 13” square x 1” Thick Bolt Circle Diameter – 9” to 14” |

| Round Pedestal Pole | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Gades Sales | 15’ Pedestal Pole | 5/5/03 |  |

### Sign Sheeting				Back to Permanent Signing Table of Contents					Back to Main

| Type XI Diamond Grade “Full Cube” Sheeting | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Avery Dennison | OmniCube Series: White: T-11500 Yellow: T-11501 Blue: T-11505 Green: T-11507 Red: T-11508 Fluorescent Yellow: T-11511 Fluorescent Yellow-Green: T-11513 | 8/25/10 | ASTM Type XI For most signs (See City of Overland Park Standard Details) Fluorescent Yellow-Green is reserved for School Zone Signing Fluorescent is reserved for special Warning Signs Yellow shall be used for all Warning Signs unless otherwise specified |
|  | 3-M | Diamond Grade Cube Corner (DG3 Series): White: 4090 Yellow: 4091 Red: 4092 Blue: 4095 Green: 4097 Fluorescent Yellow: 4081 Fluorescent Yellow-Green: 4083 Orange: 4084 | 6/23/05 |  |

| Electronic Cuttable Film | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Avery Dennison | Yellow: OL-2001 Red: OL-2008 Orange: OL-2004 Blue: OL-2005 Green: OL-2007 Brown: OL-2009 Black: OL-2003 | 5/5/03 |  |
|  | 3-M | Yellow: EC Series 1170 Red: EC Series 1172 Orange: EC Series 1174 Blue: EC Series 1175 Green: EC Series 1177 Brown: EC Series 1179 Black: EC Series 1178 | 5/5/03 |  |

### Specialty Item Approved Materials List

| Decorative Signal Poles | Light Fixtures | Light Poles | Special Screw-in Foundations |
| --- | --- | --- | --- |
| Ped Button Pole & Foundation |  |  |  |

### Decorative Signal Poles			Back to Specialty Item Table of Contents				Back to Main

| Mast Arm Poles | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| 95th St & Nall Ave | Valmont | Pole: Tapered, 16-Sharp Fluted w/ 2.875” OD x 4” L Tenon Mast Arm: Smooth Round Tapered Pole Cap: Standard |  | Color: RAL 6012 OP Green Finish: F-306 |
| Metcalf Corridor, excluding downtown node | Valmont | Pole: Tapered, 16-Sharp Fluted w/ 2.875” OD x 4” L Tenon Mast Arm: Smooth Round Tapered Pole Cap: Metro Series |  | Color: Fed-Std-595 #27038 Black Finish: F-306 |
| Oak Park Mall Signals along 95th St and Quivira; 95th & Nieman | Valmont | Standard pole and mast arm Pole Cap: Spear Series |  | Color: RAL 6012 OP Green Finish: F-306 |

| Pedestal Poles | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| 95th St & Nall Ave | Valmont | Pole: Straight, 16-Flat Fluted |  | Color: RAL 6012 OP Green |
| Metcalf Corridor, excluding downtown node | Valmont | Pole: Straight, 16-Flat Fluted |  | Color: Fed-Std-595 #27038 Black Finish: Powder Coat |
| Oak Park Mall Signals along 95th St and Quivira; 95th & Nieman | Valmont | Standard pole |  | Color: RAL 6012 OP Green Finish: Powder Coat |

| Decorative Bases for Mast Arm Poles | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Oak Park Mall Signals along 95th St and Quivira; 95th & Nieman | Valmont | Contour Series CN20AB, CN27AB & CN34AB |  | Color: RAL 6012 OP Green Finish: Powder Coat |
| 95th St & Nall Ave | Valmont | Washington Series WA25AB, WA30AB & WA36AB |  | Color: RAL 6012 OP Green Finish: Powder Coat |
| Metcalf Corridor, excluding downtown node | Valmont | Sterling Series ST24AB, ST25AB & ST31AB |  | Color: Fed-Std-595 #27038 Black Finish: Powder Coat |

| Decorative Bases for Pedestrian Poles | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Oak Park Mall Signals along 95th St and Quivira; 95th & Nieman | Valmont | Contour Series CN18AB |  | Color: RAL 6012 OP Green Finish: Powder Coat |
| 95th & Nall | Valmont | Washington Series WA18AB |  | Color: RAL 6012 OP Green Finish: Powder Coat |
| Metcalf Corridor, excluding downtown node | Valmont | Sterling Series ST18AB |  | Color: Fed-Std-595 #27038 Black Dark Bronze (Metcalf Downtown Node) Finish: Powder Coat |

### Light Fixtures					Back to Specialty Item Table of Contents				Back to Main

| Antioch & I-435 Bridge Decorative Fixture | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Bega | 8189P-Blk-120 w/ GE 12870 Fluorescent lamp | 7/21/04 | 120 Volt, Black, Fluorescent lamp |

| 110th Street & Lamar Roundabout Decorative Fixture | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Gardco Lighting | Gullwing #G18-1-2XL-400-MH-240-BLP | 4/26/02 | Type II Distribution, 400W MH, Black |

| 110th & Lamar Roundabout Landscape Fixture | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hydrel | 4710A-175M-120-SP-ISSDLA-BZ | 4/26/02 | 175W MH, Bronze |

| Antioch & I-435 Bicycle Tunnel Light Fixture; Indian Creek Bicycle Trail under I-435 | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Photometric Curve LTL16011 | Holophane | W4-100HP-MC-S-Z-F2 | 9/2/08 | 100W HPS, Dark Bronze, Type IV Distribution |

| 133rd & Lamar; 132nd Street & US-69 Overpass; Vineyards and Mills Farm Roundabouts | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| These are for replacement of existing heads only. This fixture is no longer approved. | Architectural Area Lighting | PRMSH3150HPS-Mogul-240MT-BLK-06A-1814 Sleeve | 8/28/06 | Promenade – Black Mogul base lamp and reflector system Photometric curve PRM3-H2-150HPS.IES |

| Community Center (Downtown) Parking Lot Fixture | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Wide Lite / Genlyte Company | Optra Area Luminaire Symmetric Distribution: OPP-250-S-QV-SR-SA Asymmetric Distribution: OPP-250-A-QV-SR-SA | 3/16/06 | 250W MH Segmented reflector with vertical lamp Multi-tap ballast Satin Aluminum finish Arm mount to round pole |

| Downtown OP | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Ltl05589.ies | Sentry | SGO-150HPS-240V-MT-Type III - No Finial-BK | 5/5/03 |  |

| 95th St & Nall Ave 71st St & Metcalf Ave 75th St & Metcalf Ave 87th St & Metcalf Ave | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | KIM Lighting | KIM Era Lantern 1A/LET26SCH3/400HPS240/**/BF HA33L-TM1/HF2/HAF2 This has to be a tenon mount because of the fluted signal pole shaft | 1/26/09 | Single Top Mounted, Single Curved Arm, 400W HPS, 240V, Type III Distribution TM! = Tenon Mount Ribbon Arm HF2 / HAF2 = Two Finials ** = Custom Color RAL 6012 (Hunter Green) BL (Black FED-STD-595 #27038) |

| 79th St & Metcalf Ave | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | KIM Lighting | KIM Era Lantern 1A/LET26SCH3/250HPS240/**/BF HA33L/**/HAF2 This does not require a tenon because the pole is not fluted. | 2/26/13 | Single Top Mounted, Single Curved Arm, 250W HPS, 240V, Type III Distribution HAF2 = Finial on the top arm stud ** = Custom Color Medium Bronze |

| 159th Street Bridge Over US-69 Highway | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | KIM Lighting | KIM Era Lantern FM/LEB26SCH3/400HPS240/**/TF Should accommodate 4.5” top pole O.D. w/ 0.188” wall | 12/13/10 | Post Top Flush Mounted, Single Curved Arm, Top Finial 400W HPS, 240V, Type III Distribution ** BL (Black FED-STD-595 #27038) |

| 127th Street (Metcalf Ave to Nall Ave) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | KIM Lighting | KIM Era Lantern 2B/LET26SCH3/250HPS240/**/BF Twin Bracket Arms @ 180 degrees 2B/HA33L/HAF2 | 12/13/10 | Twin Top Mounted, Single Curved Arm, Bottom Finial 250W HPS, 240V, Type III Distribution Ribbon Arm w/ top finial ** BL (Black FED-STD-595 #27038) |

| 95th St: Quivira Rd to Nieman Rd Quivira Road: 95th St to 99th St | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | KIM Lighting 95th St: Quivira to Nieman Quivira Rd: 95th St to 99th St | KIM Warp 9 HPS – Single w/2” slipfitter for Type A or B arm 1A/WP9LM3/400HPS240/CC/HSF/TB KIM Warp 9 HPS – Twin Std Arms 2B/WP9LM3/400HPS240/CC/TB KIM Warp 9 HPS – Single Std Arm 1A/WP9LM3/250HPS240/CC/TB | 8/2/09 | 250W or 400W HPS, 240V Type III Distribution CC = Custom Color (RAL 6012 Hunter Green) |

### Light Poles						Back to Specialty Item Table of Contents				Back to Main

| 110th Street & Roundabout Square Pole | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Gardco Lighting | #SSS 30-5-11-BLP | 4/26/02 | 5” square, straight, steel - Black |

| Community Center (Downtown) Parking Lot Pole | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | KW Industries | RSP18-4.0-11-NA-DM10-BC | 3/21/06 | Round Steel Satin Aluminum finish Arm mount option |

| Decorative Poles for Downtown OP and 132nd Street Bridge over US-69 Highway | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | Dwg No. C19043 – 8/3/10 | 8/5/10 | Nylon hand hole screws |

| Special Pole for 159th Street Bridge over US-69 Highway | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | Dwg No. SKKP110211B -1 11/2/11 | 11/11/11 | Shaft Length is 29’-3” or 39’-3” as specified Color: Black FED-STD-595 #27038 or Hunter Green # RAL 6012 |
|  | Valmont | Dwg No. LH30800 – 10/17/11 | 11/1/11 |  |

| Special Pole for Era Lantern Bolt Pattern 127th St (Metcalf to Nall) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | OP301-LANTERN Dwg No. SKKP110211A-001 –Single Dwg No. SKKP110211A-002 – Twin OP401-LANTERN Dwg No. SKKP012011A-001 –Single Dwg No. SKKP012011A-002 – Twin Pole Cap & Finial – F0004 | 11/11/11 | Shaft Length is 29’-3” or 39’-3” as specified Pole Cap & Finial Color: Black FED-STD-595 #27038 or Hunter Green # RAL 6012 |
|  | Valmont | OP301-LANTERN OP401-LANTERN | 11/2/11 |  |

| Special Pole for Warp9 Bolt Pattern Quivira Rd (99th to 95th) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | OP301-WARP Dwg No. SKKP110211C-001 – Single Dwg No. SKKP110211C-002 – Twin OP401-WARP Dwg No SKKP013111A-001 – Single Dwg No SKKP013111A-002 – Twin | 11/11/11 | Shaft Length is 29’-3” or 39’-3” as specified Color: Black FED-STD-595 #27038 or Hunter Green # RAL 6012 |
|  | Valmont | OP301-WARP OP401-WARP | 11/2/11 |  |

### Pedestrian Pushbutton Pole		Back to Specialty Item Table of Contents				Back to Main

| Pedestrian Pushbutton Pole and Foundation | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | AB Chance | Screw-in-Foundation: T1121363 / Dwg No. SA1121363 Ped Button Post: T1121364 / Dwg No. SA1121364 | 10/21/11 | Hot dip galvanized finished smooth. |
| Pole Base Cover | Manufacturer | Catalog Number | Approval Date | Comments |
|  | Lithonia | RSS FBC 3-5IN RND JMA 1751 DNA | 1/7/13 | ABS Plastic. Square base with 3.5” diameter hole. Two-piece cover – natural aluminum |

### Special Screw-In Foundations		Back to Specialty Item Table of Contents				Back to Main

| Screw-In Foundations for Downtown OP Pole | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | AB Chance | T112-03631701 Dwg No. SA11203631701 Rev A | 8/5/10 | Used with Hapco Decorative Pole |

# Street Lighting Approved Materials List

| Breakaway Pole Devices | Control Centers | Luminaires |  |
| --- | --- | --- | --- |
| Cable | Grounding Equipment | Photocell |  |
| Conduit and Fittings | Junction and Service Boxes | Poles |  |
| Connector Kits, Fuse Holders and Fuses | Lamps | Screw-In Foundations |  |

### Breakaway Pole Devices		Back to Street Lighting Table of Contents					Back to Main

| Break-away Couplings and Bases | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Precision Form, Inc. | PFI-200-1A Breakaway Couplings | 5/5/03 |  |
|  | Akron Foundries, Inc. / Hapco | AASHTO No. TB6-9”–10 ½” to 12½” Bolt Circle Dwg # A79402 – 4/4/98 AASHTO No. TB5-9”–14 ½” to 15¼” Bolt Circle Dwg # A79236 – 1/4/00 | 8/15/03 |  |
|  | Akron Foundries, Inc. / Valmont | CS-300 – Up to 12” Bolt Circle AASHTO No. TB6-9 Dwg # KS-90 – 5/14/03 CS-370 – 14 ½” to 15” Bolt Circle AASHTO No. TB5-9 Dwg # KS-91 w/ Rev 1 | 6/20/03 |  |

### Cable						Back to Street Lighting Table of Contents					Back to Main

| Ground Wire | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cerro Wire & Cable Co, Inc. | Product Number 050-2200 or 050-2215 | 5/5/03 | Soft Drawn Bare Solid Copper #6 AWG |
|  | Encore Wire LTD | Bare No. 6 AWG | 8/1/03 |  |
|  | Essex Electrical Products | Product Number 060062C | 8/21/03 |  |
|  | Senator / Southwire | Bare No. 6 AWG | 5/5/03 |  |
|  | Service Wire Co | Bare-CU-SD-6-7SOL | 5/7/02 |  |

| Distribution Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Member of The Marmon Group of Companies | Aetna Insulated Wire Co. | UL file # E63541 | 2/21/05 | No. 4 AWG USE Copper Black insulation Single cable, not three cables twisted on the reel |
|  | Alan Wire | Product Number 04USE11 – 500’ UL file #E319493 | 1/30/12 |  |
| Member of The Marmon Group of Companies | Cerro Wire & Cable Co, Inc. | UL file # E11098 | 5/5/03 |  |
|  | Draka Cableteq | Product Number 388932 | 7/8/09 |  |
|  | Encore Wire LTD | UL file # E174428 | 8/1/03 |  |
|  | Essex Electrical Products | Product Number 0800410 UL file # E11134 | 2/1/01 |  |
|  | Kris Tech Wire Co, Inc. | 0407-RHW/USE-BK UL file # E207249 | 11/24/03 |  |
|  | Senator / Southwire Co | 11-32-72 UL file # E32071 | 5/5/03 |  |
|  | Service Wire Co | UL file # E105667 | 5/7/02 |  |

| Pole Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cerro Wire & Cable Co, Inc. | Black – 112-3801 Red – 112-3803 Green – 112-3805 UL file # E15119 | 5/5/03 | Stranded copper THHN/THWN #10 AWG Color Coded Red and Black Green for ground cable |
|  | Encore Wire LTD | UL file # E123774 | 8/1/03 |  |
| Purchased by Southwire Co. 9/5/2001 | Essex Electrical Products | Product Number 070101 UL file # E14656 | 2/1/01 |  |
|  | Senator / Southwire Co. | Red – 22-97-57 Black – 22-97-32 Green – 22-97-xx UL file # E23919 | 5/5/03 |  |
|  | United Copper Industries | Black – 325370 (500’ reel) Red – 325372 (500’ reel) Green – 325379 (500’ reel) Black – 325573 (2,500’ reel) Red – 325574 (2,500’ reel) Green – 325580 (2,500’ reel) UL file # E194031-A | 5/26/09 |  |

| Electrical Service Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Member of The Marmon Group of Companies | Aetna Insulated Wire Co. | UL file # E63541 | 2/21/05 | No. 4 AWG USE Copper Black insulation Single cable, not three cables twisted on the reel |
|  | Alan Wire | Product Number 04USE11 – 500’ UL file #E319493 | 1/30/12 |  |
| Member of The Marmon Group of Companies | Cerro Wire & Cable Co, Inc. | UL file # E11098 | 5/5/03 |  |
|  | Draka Cableteq | Product Number 388932 | 7/8/09 |  |
|  | Encore Wire LTD | UL file # E174428 | 8/1/03 |  |
|  | Essex Electrical Products | Product Number 0800410 UL file # E11134 | 2/1/01 |  |
|  | Kris Tech Wire Co, Inc. | 0407-RHW/USE-BK UL file # E207249 | 11/24/03 |  |
|  | Senator / Southwire Co | 11-32-72 UL file # E32071 | 5/5/03 |  |
|  | Service Wire Co | UL file # E105667 | 5/7/02 |  |

### Conduit and Fittings			Back to Street Lighting Table of Contents					Back to Main

| PVC Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cantex | 1” – A52BA12 2” – A52CA12 | 5/5/03 | Schedule 40 PVC |
|  | Certain Teed | 1” – 27213 1 ½” – 27413 2” – 27513 3” – 27713 4” – 27913 | 5/5/03 |  |
|  | Heritage Plastics | 1” – 511010 – 10’ or 511020 – 20’ 1 ½” – 511510 – 10’ or 511520 – 20’ 2” – 512010 – 10’ or 512020 – 20’ 3” – 513010 – 10’ or 513020 – 20’ 4” – 514010 – 10’ or 515020 – 20’ | 7/24/12 |  |
|  | IPEX / PW Eagle | 1” – 032410 – 10’or 032411 – 20’ 2” – 032420 – 10’ or 032421 – 20’ 3” – 032430 – 10’ or 032431 – 20’ 4” – 032440 – 10’ or 032441 – 20’ | 12/22/05 |  |
| Formerly Carlon | Prime Conduit | 1” – 49008-010 (10’ length) 1” – 49008-020 (20’ length) 2” – 49011-010 (10’ length) 2” – 40911-020 (20’ length) 3” – 49013-010 (10’ length) 3” – 49013-020 (20’ length) | 5/26/09 |  |
|  | Rocky Mountain Colby Pipe | 2” – 502010U – 10’ or 502020U – 20’ 3” – 503010U – 10’ or 503020U – 20’ 4” – 504010U – 10’ or 504020U – 20’ | 4/7/09 |  |

| PVC Fittings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cantex | Standard Couplings: 1” – 6141625 2” – 6141628 90º Elbows: (Plain End / Belled End) 1” – 5133825 / 5233825 2” – 5133828 / 5233828 45º Elbows: (Plain End / Belled End) 1” – 5133765 / 5233765 2” – 5133768 / 5233768 30º Elbows: (Plain End / Belled End) 1” – 5133745 / 5233745 2” – 5133748 / 5233748 | 5/5/03 | Schedule 40 PVC |
|  | Heritage Plastics | Standard Couplings: 1” – 59603 2” – 59606 90º Elbows: (Plain End / Belled End) 1” – 59590 / 59374 2” – 59593 / 59377 45º Elbows: (Plain End / Belled End) 1” – 59577 / 59386 2” – 59580 / 59389 30º Elbows: (Plain End / Belled End) 1” – 59563 / 59367 2” – 59566 / 60249 | 7/24/12 |  |
|  | IPEX / PW Eagle | Standard Couplings: 1” – EC20 / 077003 2” – EC35 / 077006 90º Elbows: (Plain End / Belled End) 1” – 068582 / 068422 2” – 068585 / 068425 45º Elbows: (Plain End / Belled End) 1” – 068602 / 068563 2” – 068605 / 068566 30º Elbows: (Plain End / Belled End) 1” – 068622 / EE2030 2” – 068625 / EE3530 | 12/22/05 |  |
|  | Plastic Trends / Royal Pipe Systems | Standard Couplings: 1” – E010100 2” – E010200 90º Elbows: (Plain End / Belled End) 1” – E018100 / E021100 2” – E018200 / E021200 45º Elbows: (Plain End / Belled End) 1” – E019100 / E022100 2” – E019200 / E022200 30º Elbows: (Plain End / Belled End) 1” – E020100 / E072100 2” – E020200 / E072200 | 1/8/10 |  |
| Formerly Carlon | Prime Conduit | Standard Couplings: 1” – E940F 2” – E940J 90º Elbows: (Plain End / Belled End) 1” – UA9AF / UA9AFB 2” – UA9AJ / UA9AJB 45º Elbows: (Plain End / Belled End) 1” – UA7AF / UA7AFB 2” – UA7AJ / UA7AJB 30º Elbows: (Plain End / Belled End) 1” – UA6AF / UA6AFB 2” – UA6AJ / UA6AJB | 5/26/03 |  |

| HDPE Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Dura-Line now owns Arnco, Boreflex, Carlon and Lamson Pipe | Dura-Line | 2” – SW 400 200 N088 3” – SW 400 300 N088 | 8/2/01 | 2” Schedule 40 Gray color Smooth outside wall, waved ribbed inside wall UV Stabilized |

| HDPE Service Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Dura-Line now owns Arnco, Boreflex, Carlon and Lamson Pipe | Dura-Line | 2” – 2SDR135BWRSWAVEIN 3” – 3SDR135BWRSWAVIN | 3/8/13 | SDR 13.5 Black with red stripes Smooth outside wall, wave rib inside wall UV Stabilized |

| HDPE Couplings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | American Ploywater | Bonduit Conduit Adhesive Use only with Cantex Sch 40 PVC Longline Couplings: 2” – 6202000 3” - 6202005 | 10/11/10 |  |
|  | Cabletec | AS 2.375 – 2” AS 3.500 – 3” | 8/2/01 |  |
|  | Central Plastics Company | Electrofusion Couplings 2” IPS 575-0042 3” IPS 575-0043 | 5/5/06 |  |
|  | Dura-Line | PushLock Couplings 1-908353 – 2” | 10/5/10 |  |
|  | Tyco Electronics / Jackmoon | Moon-Link Transparent Duct Coupling 2” – 20TC238SP 3” – 30TC350SP | 12/23/02 |  |
|  | Unitex | Pro-Poly CA Adhesive Use only with Cantex Sch 40 PVC Longline Couplings: 2” – 6202000 3” – 6202005 | 1/9/06 |  |

### Connector Kits, Fuse Holders

### and Fuses					 Back to Street Lighting Table of Contents					Back to Main

| Multi-tap Connectors | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Connector MFG.Co. | CMC SLK-112 I | 1/11/01 | 6061-T6 aluminum Provide rubber boot cover – black plastisol |
|  | Fargo Mfg. Company, Inc subsidiary of Hubbell Inc. | Fargo GO-32 | 5/5/03 |  |
|  | Polaris | SLCS4A-4P | 9/21/07 | Coated w/ allen head screw – does not need rubber boot |

| Un-Fused Fuse Holders | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Ideal Industries purchased Buchanan | Ideal Industries / Buchanan / Elastimold | Style 20 U Breakaway | 5/5/03 | Single pole in-line non-fused 600 volt, 30 amp Copper #10 AWG conductor size |

| Fused Fuse Holders | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Ideal purchased Buchanan | Ideal Industries / Buchanan / Elastimold | Style 65 U Breakaway | 5/5/03 | Single pole in-line fused 600 volt, 8 amp Copper #10 AWG conductor size |

| Fuses | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Bussmann Circuit Protection, Worldwide | Buss Type KTK8 | 5/5/03 | 600 volt, 8 amp |
|  | Ferraz Shawmut | ATM-8 | 1/25/02 |  |
|  | Littelfuse | KLK-8 | 7/31/01 |  |

| Splice Kits | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Burndy | Split-Bolt Connectors KS20 - #8 STR to #4 STR KS22 - #6 STR to #3 STR KS23 - #6 STR to #2 STR KS25 - #4 STR to #1/0 STR Copper Compression Tees YST4C4 - #4 STR to #4 STR | 5/5/03 |  |
|  | NSI Industries Polaris Blue | ISW-4 - #4 two-port in-line splice ITW-4 - #4 two port IPLW4-3 - #4 three port IPLW4-3 - #4 four port | 9/11/07 | Waterproof / submersible |

### Control Centers				Back to Street Lighting Table of Contents					Back to Main

| Control Centers (Four-Circuit) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Milbank | CP3B91115PAOOP4 | 4/8/11 | Ringless meter cover with horn bypass and exposed meter |
|  | Myers Electric Products, Inc. | MEUG16AR-M100-OPK | 7/24/12 |  |
| Purchased by Myers 12/10/12 | Pacific Utility Products | USP16R-M2100-112C-AL-OPK | 2/3/11 |  |

| Control Centers (Single-Circuit) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Milbank | Pending approval |  | Ringless meter cover and horn bypass with mounting collar for stand alone unit. |
|  | Myers Electric Products, Inc. | MET2-VLM-LTS-R | 7/24/12 |  |
| Purchased by Myers 12/10/12 | Pacific Utility Products | USP2R-100-112C-OPK-LT-PM | 2/17/12 |  |

### Grounding Equipment			Back to Street Lighting Table of Contents					Back to Main

| Ground Rod | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Chance/Hubbell | Cat No. C611300 | 4/24/12 | ½” x 10’-0” long Copper clad steel core UL listed |
|  | Erico Inc. / Eritech | Cat. No. 611300 – ½” x 10’ Cat. No. 613400 – ¾” x 10’ | 2/27/02 |  |
|  | ITTBlackburn | Cat. No. 5010 | 5/5/03 |  |
|  | Joslyn | Cat No. J-8330 | 5/5/03 |  |
|  | Knight | GRC 1210 | 5/5/03 |  |

| Ground Rod Clamp | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Burndy | GRC 12 – ½” GRC34 – ¾” | 2/27/02 | Hex head set screw Copper alloy Long bearing surface UL listed |
|  | Erico Inc. / Eritech | Part No. HDC12 – ½” Part No. HDC34 – ¾” | 12/1/05 |  |
|  | ITT Blackburn | Type JAB-12H | 5/5/03 |  |

### Junction and Service Boxes 		Back to Street Lighting Table of Contents					Back to Main

| Type I Junction Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001423TA (12” x 12” x 12”) | 1/11/01 | Logo to read “Street Lighting” Cover to be ¾” thick (CDR is 1 ½” thick) Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers |
|  | CDR | SB33-1212-12 – Box only SC30-1212-02 – Cover only SA33-1212-12 – Assembly | 5/19/95 |  |
|  | Carson Industires | HLW1212-12 – Box only HLW1212-P0 – Cover only | 6/29/04 |  |
|  | Highline | PHB121212 – Box only CHC1212SL – Cover only PHA121212SL2 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 121212PCB – Box only 1212PCC – Cover only 121212PC – Assembly | 10/17/11 |  |
|  | New Basis | PCB121212A04 – Box only PCC121212A04 – Cover only PCA121212A4009 – Assembly | 2/26/02 |  |
|  | Quazite | PC1212BA12 – Box only PC1212CA0041 – Cover only | 5/5/03 |  |

| Type II Junction Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001429TA (11”x18”x12”) | 7/30/01 | Logo to read “Street Lighting” Cover to be 1 ¾” to 2” thick Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers |
|  | Carson Industires | H1118-12 – Box only H1118-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-1118-12 – Box only SC30-1118-02 – Cover only SA33-1118-12 – Assembly | 5/19/95 |  |
|  | Highline | PHB111812 – Box only CHC1118SL – Cover only PHA111812SL2 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 111812PCB – Box only 1118PCC – Cover only 111812PC – Assembly | 10/17/11 |  |
|  | New Basis | PCB111812A04 – Box only PCC111812A04 – Cover only PCA111812A866 – Assembly | 2/26/02 |  |
|  | Quazite | PG1118BA12 – Box only PG1118CA0041 – Cover only | 5/5/03 |  |

### Lamps					 Back to Street Lighting Table of Contents					Back to Main

| High Pressure Sodium | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | General Electric | Lucalox – HPS lamps 100 W – LU100/ECO/NC – 14673 150 W – LU150/55/ECO/NC – 40390 250 W – LU250/ECO/NC – 14674 400 W – LU400/ECO/NC – 14675 | 11/4/10 | Clear lamp Mogul base ECO/ALTO = Low Mercury NC = Non Cycling 30,000+ Hour Average Life |
|  | Phillips | 100 W – C100S54/ALTO/NC – 14740-5 150 W – C150S55/ALTO/NC – 14741-3 250 W – C250S50/ALTO/NC – 14742-1 400 W – C400S51/ALTO/NC – 14743-9 | 10/14/11 |  |
|  | Sylvania | Lumalux PLUS/ECO – HPS lamps 100 W – LU100/PLUS/ECO – 67559 150 W – LU150/55/PLUS/ECO – 67494 250 W – LU250/PLUS/ECO – 67572 400 W – LU400/PLUS/ECO – 67312 | 3/26/08 |  |

### Luminaires					 Back to Street Lighting Table of Contents					Back to Main

| Cobra-Head Luminaire | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Photometric Curves 150:AE7361-70fg3.ies 250 & 400: AEL12963.ies | American Electric Lighting – Acuity Brands | 31515SCAMT2R3FGM2NRHPAR8663 – 150W HPS 32525SCAMT2R3FGNRHPAR8037 – 250W HPS 32540SCAMT2R3FGNRHPAR8037 – 400W HPS | 4/28/05 4/15/05 | 2-Bolt slip fitter connection for 150 W fixtures 4-Bolt slip fitter connection large housing for 250 W and 400 W fixtures Multi-Tap Ballast Plug-In “Protected” starter Aluminum wildlife guard NO PHOTOCELL |
| Photometric Curves 150: OVF15S2D 250: OVF25S3D 400: OVF40S3D | Cooper | OVF15SWV3D-U1114 – 150W HPS OVF25SWV3D-U1112 – 250W HPS OVF40SWV3D-U1113 – 400W HPS | 2/7/05 |  |
| Photometric Curves 150: GE7285.ies 250 & 400: GE1002.ies or GE7323.ies | General Electric | M2AC15S0A1GMC31347 – 150W HPS MDCA25S0A12FMC31 – 250W HPS MDCA40S0A12FMC31 – 400W HPS | 5/5/03 |  |
| 150 & 250: HP03116.ies 400: HP03065.ies | Hubbell | RMCD15S38031125F0M53-150W RMCD25S38031125F0M53-250W RLCD40S38031125F0M53-400 W | 5/5/03 |  |

| Highway Luminaire | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Photometric Curve 400W: 452580.ies | General Electric | RPFT40S0A1GLN4GR – 400W HPS | 5/5/03 |  |

| Residential Post Top | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Photometric Curves 100 & 150 W: 42737 | Holophane | PTU-10DHP-MT-B-P3-B-P – 100 W PTU-15DHP-MT-B-P3-B-P – 150 W | 2/14/03 | Multi-Tap Ballast |
| Photometric Curves mpb15s3a – Type 3 mpb15sa – Type 5 | Sentry | SLH-100HPS-240MT-BLAF –Type 3 SLH-150HPS-240MT-BLAF –Type 3 SLH-100HPS-240MT-BLSF –Type 5 | 5/5/03 |  |

### Photocell					 Back to Street Lighting Table of Contents					Back to Main

| System Photocell | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Dark To Light (DTL) | DP124-0.2-1821 | 3/27/13 | 120Volt, Turn on at 0.2 Fc Silicon Chip |

### Poles						Back to Street Lighting Table of Contents					Back to Main

| Aluminum Poles 30’ Mounting Heights | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | 27’-6” Poles: Dwg # B84165-001 – Type OP301 w/single 6’ arm – 10/04 Rev 1 Dwg # B84165-002 – Type OP301 w/single 8’ arm – 10/04 Rev 1 Dwg # B79636-001 – Type OP302 w/single 12’ arm – 10/04 Rev 2 Dwg # B84165-003 – Type OP303 w/twin single member 8’ arms – 10/04 Rev 1 Dwg # B79636-005 – w/twin 8’ truss arms – 10/04 Rev 2 Identification Label: Dwg # B84166 9-3-03 | 11/1/04 | J-hook at top of pole Handhole cover keeper chain attached to bottom of handhole opening or Hinged handhole option Grounding screw shaft installed parallel to pole shaft at back side of pole. Labeled with manufacturer identification tag. 0.188” Wall Thickness Cable hook at top of pole |
|  | Valmont | 27’-6” Poles: Dwg # KS-71 – Type OP301 w/Rev 2 Dwg # KS-72 – Type OP302 w/Rev 2 Dwg # KS-73 – Type OP303 w/Rev 2 Handholes: Dwg # KS-86 – Type OP301 w/Rev 2 Dwg # KS-86 – Type OP302 w/Rev 2 Dwg # KS-87 – Type OP303 Identification Label: Dwg # KS-89 and KS-89A | 9/13/05 |  |

| Aluminum Poles 40’ Mounting Heights | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | 37’-6” Poles: Dwg # 84165-004 – Type OP401 w/single 6’ arm – 10/04 Rev 1 Dwg # 84165-005 – Type OP401 w/single 8’ arm – 10/04 Rev 1 Dwg # B79636-002 – Type OP402 w/single 10’ arm – 10/04 Rev 2 Dwg # B79636-003 – Type OP402 w/single 12’ arm – 10/04 Rev 2 Dwg # B79636-004 – Type OP402 w/single 15’ arm – 10/04 Rev 2 Dwg # 80061-001 Type OP403 w/twin 12’ & 8’ arms – 10/04 Rev 3 Dwg # 80061-002 Type OP403 w/twin 12’ arms – 10/04 Rev 3 Dwg # 80061-003 Type OP403 w/twin 15’ arms – 10/04 Rev 3 Dwg # 80061-004 Type OP403 w/twin 10’ arms – 10/04 Rev 3 Identification Label: Dwg # B84166 9-3-03 | 11/1/04 | J-hook at top of pole Handhole cover keeper chain attached to bottom of handhole opening or Hinged handhole option Grounding screw shaft installed parallel to pole shaft at back side of pole. Labeled with manufacturer identification tag. 0.219” Wall Thickness Cable hook at top of pole |
|  | Valmont | 37’-6” Poles: Dwg # KS-74 – Type OP401w/Rev 2 Dwg # KS-75 – Type OP402 w/Rev 3 Dwg # KS-76 – Type OP403 w/Rev 3 Handholes: Dwg # KS-87 – Type OP401 w/Rev 2 Dwg # KS-87 – Type OP402 w/Rev 2 Dwg # KS-88 – Type OP403 w/Rev 1 Identification Label: Dwg # KS-89 & KS-89A | 9/13/05 |  |

| Aluminum Street Light Bracket Arms | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | Information Contained on Pole Drawings. | 9/3/03 9/3/03 | Supply end cap on lower truss member. Labeled with identification tag. |
|  | Valmont | Arms: Dwg # KS-77 – 6’ Single – 5/14/03 Dwg # KS-78 – 8’ Single – 5/14/03 Dwg # KS-79 – 8’ Truss – 5/14/03 Dwg # KS-80 – 10’ Truss – 5/14/03 Dwg # KS-81 – 12’ Truss – 5/14/03 Dwg # KS-82 – 15’ Truss – 5/14/03 Arm Attachment: Dwg # KS-83 – Single w/Rev 1 Dwg # KS-84 – Truss w/Rev 1 | 11/29/04 |  |

| Aluminum Poles 14’ Mounting Heights | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hapco | Dwg # A66338 w/Rev # 10 – 4/08 | 4/23/08 | Handhole cover keeper chain attached to bottom of handhole opening. Handhole should be smooth and free of burs. Grounding screw shaft installed parallel to pole shaft at back side of pole. Labeled with manufacturer identification tag. 0.156” Wall Thickness |
|  | Valmont | Dwg # KS-70 – Type OP14 w/Rev 5 Dwg # KS-85 – Handhole w/Rev 1 Dwg # KS-89 – ID Detail | 4/23/08 |  |

### Screw-In Pole Foundations		 Back to Street Lighting Table of Contents					Back to Main

| Screw-in Foundations | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | AB Chance | T112-0363 – R OP14 T112-0748 – T1 OP301/302/303 T112-02930101 – F1 OP401/402 T112-02940101 – F2 OP403 | 2/20/06 | Manufacturer and foundation identification stenciled on base plate with ¼” to ½” lettering. |
|  | Dixie | D-1202-0029-A – R OP14 D-1202-0465-A – T1 OP301/302/303 D-1202-0031-A – F1 OP401/402 D-1202-0032-A – F2 OP403 | 10/17/03 |  |
|  | Earth Contact Products | LPS-66T-048-12 – R OP14 LPS-66T-060-12 – T1 OP301/302/303 LPS-86T-60A-14 – F1 OP401/402 LPS-86T-60B-14 – F2 OP403 | 10/15/12 |  |
|  | JH Botts, Inc. | Dwg # JHBOPK-1 w/Rev A | 8/20/03 |  |
|  | Pelco | SK-1094-1 Rev C – R OP14 SK-1109-1 Rev B – T1 OP301/302/303 SK-1108-1 Rev B – F1 OP401/402 SK-1095-1 Rev E – F2 OP403 | 7/19/06 |  |

# Traffic Control Approved Materials List

| Arrow Panels | Channelizing Devices | Temporary Marking |  |
| --- | --- | --- | --- |
| Barricades | Inertial Barrier Systems | Warning Lights |  |
| Changeable Message Signs | Sign Sheeting |  |  |

### Arrow Panels				Back to Construction Traffic Control Table of Contents				Back to Main

| Arrow Panels | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | National Signal | Sunup Solar Arrow Panel | 3/14/05 |  |
|  | Solar Technology, Inc. | Silent Sentinel | 3/26/13 |  |
|  | Wanco, Inc. | WTSP75-LSAC | 3/14/05 |  |

### Barricades					Back to Construction Traffic Control Table of Contents				Back to Main

| Type I Barricades | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | TrafFix Devices, Inc. | WZ-46 Federal Acceptance Number |  |  |

| Type II Barricades | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Plastic Safety Systems | The Wave – 24” The Wave – 36” |  |  |

| Type III Barricades | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Davidson Traffic Control Products | T3B Barricade – Type 9 Prismatic HI (VIP DG) | 11/8/12 | High Intensity Prismatic Sheeting |
|  | Plastic Safety Systems | The Wave – Centerboard The Mast – Upright Anchor Base – Base | 11/8/12 |  |

| ADA Pedestrian Barricades | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Plastic Safety Systems | Safety Wall | 11/8/12 | Continuous smooth upper rail No gaps between sections Vertical plane without obstructions Lower rail 2” or less above ground Upper rail not less than 32” high |

### Changeable Message Signs		Back to Construction Traffic Control Table of Contents				Back to Main

| Changeable Message Signs | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Addco | Model DH 1000 ALS |  |  |
|  | Solar Tech | Silent Messenger Model MB-3048 |  |  |

### Channelizing Devices			Back to Construction Traffic Control Table of Contents				Back to Main

| Conical Delineator / Trim Line Cone | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Lakeside Plastics, Inc. | The Diverter | 11/9/12 | 42” Tall 2 – 6” Fluorescent Orange Prismatic Bands 2 – 6” White High Intensity Bands |
|  | Plastic Safety Systems | Navigator Channelizer | 2/26/13 |  |
|  | TrafFix Devices, Inc. | Grabber Cone 42266-CRU-16DGDG | 2/26/13 |  |

| Drums | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Lakeside Plastics, Inc. | The Director | 2/26/13 | High Prismatic Sheeting |
|  | Plastic Safety Systems | LifeGard Traffic Drum LifeGard II Traffic Drum | 2/26/13 |  |
|  | TrafFix Devices, Inc. | Series 18000 | 2/26/13 |  |

### Inertial Barrier Systems		Back to Construction Traffic Control Table of Contents				Back to Main

| Sand Barrels | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Energy Absorption Systems, Inc. | Energite III |  |  |

### Sign Sheeting				Back to Construction Traffic Control Table of Contents				Back to Main

| Sign Sheeting | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Avery Dennison | Fluorescent Orange – W-7514 High Intensity White – T-6500 |  | Prismatic Type Sheeting |
|  | 3M | High Intensity White – 3930 |  |  |

### Temporary Markings			Back to Construction Traffic Control Table of Contents				Back to Main

| Waterborne Paint | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Ennis Paint | EP Series Fast Dry |  |  |

| Removable Tape | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Swarco Industries | Director 2 | 3/9/12 |  |

| Non-Removable Tape | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Swarco Industries | Visa Line | 3/9/12 |  |

### Warning Lights				Back to Construction Traffic Control Table of Contents				Back to Main

| Warning Lights | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | C & C Signal LLC | Eclipse Solar Type A/C |  |  |
|  | Empco-Lite | Model 499L3 Type B / 747A LED Type A / 100 LED Model 212 B-Lite |  |  |

# Traffic Signal Approved Materials List

| Backplates | Grounding Equipment | Mounting Brackets | Wire Connectors |
| --- | --- | --- | --- |
| Cable | Junction and Service Boxes | Poles |  |
| Conduit and Fittings | LED Units | Power Backup Systems |  |
| Controller Cabinet | Loop Sealants | Secondary Service Pedestals |  |
| Detection Systems | Miscellaneous Controller Equipment | Signal Heads |  |

### Backplates					Back to Traffic Signal Table of Contents						Back to Main

| Backplates (Vehicular) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Gades Sales / Neodesha Plastics | BP481PO – 1 section BP483PO – 3 section BP484PO – 4 section BP485PO – 5 section | 5/5/03 | 0.125” thick 12” Signal Head Sections |
|  | Mid American Signal | MI-1003-L2 – 3 section for Econolite MI-1003-N – 3 section for McCain | 5/5/03 |  |
|  | Pelco Products, Inc. | BK-1001-L3 – 1 section for Econolite BK-1003-L3 – 3 section for Econolite BK-1004-L3 – 4 section for Econolite BK-1005-L3 – 5 section for Econolite BK-1001-N – 1 section for McCain BK-1003-N – 3 section for McCain BK-1004-N – 4 section for McCain BK-1005-N – 5 section for McCain | 5/5/03 |  |

### Cable 					Back to Traffic Signal Table of Contents						Back to Main

| Video Detection Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Econolite Exclusive | Falcon Fine Wire | 970316TS-00-1MP | 1/30/12 | 16 AWG/3c |
| Econolite Exclusive | Isotec | X339313-00 (for Econolite Solo Terra Systems) | 4/25/08 |  |
| For use with ITS Plus3 signal mount camera only | Belden | 9259 75 Ohm | Under Trial and Review |  |

| CCTV Camera Cat 5e Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Use with IP HD CCTV Camera | Comscope | 8840305/10 | 11/1/11 | 4 pair 24 AWG with shield and drain wire. (Gray insulation) Requires an RJ-45 Plug in Data Protector (see Grounding Equipment) |

| CCTV Camera Communication Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| USED ONLY FOR MAINTENANCE ON PELCO CCTV DOME CAMERA SYSTEMS | Belden | 8281F 75 Ohm (for CCTV Cameras) with 75 Ohm Connectors | 2/1/01 | Coaxial Cable |

| CCTV Camera Pan-Tilt-Zoom Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| USED ONLY FOR MAINTENANCE ON PELCO CCTV DOME CAMERA SYSTEMS | Belden | 9843 | 6/17/03 |  |

| CCTV Camera Power Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| USED ONLY FOR MAINTENANCE ON PELCO CCTV DOME CAMERA SYSTEMS | Advanced Digital Cable / Clifford of Vermont | 8103/3C14B7119-1 | 5/5/03 | 1-3c#14 IMSA 19-1 |
|  | Falcon Fine Wire | 980314X19-1-00 | 4/24/08 |  |
|  | Southwire | #14 AWG stranded copper | 7/15/08 |  |

| CNG Monitoring Cable / Illuminated Street Name Sign Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Advanced Digital Cable / Clifford of Vermont | 8103/3C14B7119-1 | 5/5/03 | 1-3c#14 IMSA 19-1 |
|  | Falcon Fine Wire | 980314X19-1-00 | 4/24/08 |  |

| CNG Power Cable 1-3c #2 AWG | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Coleman Cable Inc. | 41112 MTW Cable | 11/5/12 | 600 Volt Copper soft drawn stranded copper #2 AWG |
|  | Southwire | #2 AWG stranded copper |  |  |
|  | Service Wire Co | XLP-USE-2-STR-BLK |  |  |

| Induction Loop Cable 1c #14 | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Advanced Digital Cable | 8450 | 6/29/09 | IMSA Type 51-5 Tube Loop Detector Cable PVC/nylon Insulated cable PVC Tube 600 Volt |
|  | Belden | 580206 | 6/17/03 |  |
| Supplier | Clifford of Vermont | 1C14B19LOOP | 5/5/03 |  |
|  | Falcon Fine Wire | 14-1 IMSA 51-5 | 4/20/01 |  |
|  | James Monroe Wire and Cable Corporation | IMSA 51-5 | 9/1/99 |  |
|  | Kris-Tech | 1419-THHN-TUBE-PVC-BLACK | 2/1/01 |  |

| Multi-conductor 7c#14 and 2c #14 | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Advanced Digital Cable / Clifford of Vermont | 7c – 8107 / 7C14B7I19-1 2c – 8102 / 2C14B7I19-1 | 5/5/03 | IMSA 19-1 600 Volt Stranded Copper #14 AWG |
|  | Belden | 7c – 601205 2c – 601457 | 2/1/01 |  |
|  | Coleman Cable Inc. | 7c – 559107 2c - 559102 | 1/10/12 |  |
|  | Falcon Fine Wire | 7c – 980714X19-1-00 2c – 980214X19-1-00 | 5/23/05 |  |
|  | James Monroe Wire and Cable Corporation | 7c – IMSA 19-1 2c – IMSA 19-1 | 9/1/99 |  |

| Micro loop Home Run | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | 3M | Model Canoga 30003 | 5/20/03 |  |

| Non-Invasive Micro loop Home Run Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Global Traffic Technologies bought out 3M | Global Traffic Technologies / 3M | Model Canoga 30003 | 2/18/08 |  |

| Emergency Vehicle Pre-emption (EVP) Detector Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Belden | 580461 – Model 138 | 11/7/05 |  |
| Global Traffic Technologies bought out 3M | 3M | Model 138 | 3/24/08 |  |

| Radar Detector Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Allied Wire & Cable | 091102WGP12 | 1/10/11 | 3 pair 22 AWG communication wires (blue, blue/white, orange, orange/white) 2 pair 20 AWG power wires (red and black) |
|  | Orion Wire / Wavetronix | WX-SS-H705 (Home Run Cable) WX-SS-H704-100 (Harness Cable) | 1/10/11 |  |

| Shielded Detector Lead-in 2c #14 | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Advanced Digital Cable | 8780 | 6/29/09 | IMSA Type 50-2 Loop Lead-in Cable Polyethylene Insulated 600 Volt Stranded Copper #14 AWG |
|  | Belden | 601765 | 2/1/01 |  |
| This is actually a Belden Cable | Clifford of Vermont | 1P14T19I50-2 | 5/5/03 |  |
|  | Falcon Fine Wire | 98021450-2 | 5/5/06 |  |
|  | General Cable | C2550 | 5/5/03 |  |
|  | James Monroe Wire and Cable Corporation | JM43465 | 9/1/99 |  |

| #10 AWG System Ground Wire and Tracer Wire | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cerowire Wire & Cable Co., Inc. | Red – 112-3803 Green – 112-3805 UL file # E15119 | 5/5/03 | Stranded copper #10 AWG THHN 600 volt Tracer wire shall have Red insulation Ground wire shall have Green insulation |
|  | Encore Wire LTD | UL file # E123774 | 8/1/03 |  |
| Purchased by Southwire Co. | Essex Group, Inc. | Product Number 070101 UL File # E14656 | 2/1/01 |  |
|  | Senator / Southwire | 22-97-57 UL file # E23919 | 5/5/03 |  |
|  | Service Wire | UL file # E105667 | 5/7/02 |  |
|  | United Copper Industries | Red – 325372 (500’ reel) Green – 325379 (500’ reel) Red – 325574 (2,500’ reel) Green – 325580 (2,500’ reel) UL file # E194031-A | 5/26/09 |  |

| #6 AWG Equipment Ground Wire | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cerro Wire & Cable Co, Inc. | Product Number 050-2200 or 050-2215 | 5/5/03 | Bare copper soft drawn solid copper #6 AWG |
|  | Encore Wire LTD | Bare No. 6 AWG | 8/1/03 |  |
|  | Essex Electrical Products | Product Number 060062C | 8/21/03 |  |
|  | Senator / Southwire | Bare No. 6 AWG | 5/5/03 |  |
|  | Service Wire Co | Bare-CU-SD-6-SOL | 5/7/02 |  |

| Electrical Service Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Member of The Marmon Group of Companies | Aetna Insulated Wire Co. | UL file # E63541 | 2/21/05 | No. 4 AWG USE Copper Black insulation Single cable, not three cables twisted on the reel |
|  | Alan Wire | Product Number 04USE11 – 500’ UL file #E319493 | 1/30/12 |  |
| Member of The Marmon Group of Companies | Cerro Wire & Cable Co, Inc. | UL file # E11098 | 5/5/03 |  |
|  | Draka Cableteq | Product Number 388932 | 7/8/09 |  |
|  | Encore Wire LTD | UL file # E174428 | 8/1/03 |  |
|  | Essex Electrical Products | Product Number 0800410 UL file # E11134 | 2/1/01 |  |
|  | Kris Tech Wire Co, Inc. | 0407-RHW/USE-BK UL file # E207249 | 11/24/03 |  |
|  | Senator / Southwire Co | 11-32-72 UL file # E32071 | 5/5/03 |  |
|  | Service Wire Co | UL file # E105667 | 5/7/02 |  |

### Conduit and Fittings 			Back to Traffic Signal Table of Contents						Back to Main

| HDPE Signal Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Dura-Line now owns Arnco, Boreflex, Carlon and Lamson Pipe | Dura-Line | 1” – SW 400 100 N029 1 ½” – SW 400 150 N029 2” – SW 400 200 N029 3” – SW 400 300 N029 4” – SW 617 400 N029 | 3/31/03 | Schedule 40 HDPE for all sizes under 4” SDR 13.5 for 4” diameters Red with 3 longitudinal white stripes Smooth outside wall, wave rib inside wall UV Stabilized |

| HDPE Service Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Dura-Line now owns Arnco, Boreflex, Carlon and Lamson Pipe | Dura-Line | 2” – 2SDR135BWRSWAVEIN 3” – 3SDR135BWRSWAVIN | 3/8/13 | SDR 13.5 Black with red stripes Smooth outside wall, wave rib inside wall UV Stabilized |

| HDPE Couplings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | American Polywater | Bonduit Conduit Adhesive Use only with Cantex Longline PVC Sch 40 Couplings: 2” Coupling – 6202000 3” Coupling – 6202005 4” Coupling – 6202010 | 10/11/10 |  |
|  | ARNCO | IA 551-150U – 1 ½” IA 551-200U – 2” | 7/31/01 |  |
|  | Cabletec | AS 2.375 – 2” AS 3.500 – 3” | 8/2/01 |  |
|  | Central Plastics Company | Electrofusion Couplings 1 ½” IPS 575-0105 2” IPS 575-0042 3” IPS 575-0043 4” IPS 575-0044 | 5/5/06 |  |
|  | Dura-Line | PushLock Couplings 1-908356 – 1” 1-908354 – 1 ½” 1-908353 – 2” | 10/5/10 |  |
|  | Tyco Electronics / Jack Moon | Moon-Link Transparent Duct Coupling 1” – 10TC132SP 1 ½” – 15TC190SP 2” – 20TC238SP 3” – 30TC350SP 4” – 40TC450SP or 40TC435SP | 12/23/02 |  |
|  | Unitex | Pro-Poly CA Adhesive Use only with Cantex Longline PVC Sch 40 Couplings: 2” Coupling – 6202000 3” Coupling – 6202005 4” Coupling – 6202010 | 1/9/06 |  |

| PVC Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cantex | 1” – A52BA12 1 ½” – A52BE12 2” – A52CA12 3” – A52DA12 4” – A52EA12 | 5/5/03 | Schedule 40 |
|  | Certain Teed | 1” – 27213 1 ½” – 27413 2” – 27513 3” – 27713 4” – 27913 | 5/5/03 |  |
|  | Heritage Plastics | 1” – 511010 – 10’ or 511020 – 20’ 1 ½” – 511510 – 10’ or 511520 – 20’ 2” – 512010 – 10’ or 512020 – 20’ 3” – 513010 – 10’ or 513020 – 20’ 4” – 514010 – 10’ or 515020 – 20’ | 7/24/12 |  |
|  | IPEX / PW Eagle | 1” – 032410 – 10’or 032411 – 20’ 2” – 032420 – 10’ or 032421 – 20’ 3” – 032430 – 10’ or 032431 – 20’ 4” – 032440 – 10’ or 032441 – 20’ | 12/22/05 |  |
| Formerly Carlon | Prime Conduit | 1” – 49008-010 (10’ length) 1” – 49008-020 (20’ length) 1 ½” – 49010-010 (10’ length) 1 ½” – 49010-020 (20’ length) 2” – 49011-010 (10’ length) 2” – 40911-020 (20’ length) 3” – 49013-010 (10’ length) 3” – 49013-020 (20’ length) 4” – 49015-010 (10’ length) 4” – 49015-020 (20’ length) | 5/26/09 |  |
|  | Rocky Mountain Colby Pipe | 2” – 502010U – 10’ or 502020U – 20’ 3” – 503010U – 10’ or 503020U – 20’ 4” – 504010U – 10’ or 504020U – 20’ | 4/7/09 |  |

| PVC Fittings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cantex | Standard Couplings: 1” – 6141625 1 ½” – 6141627 2” – 6141628 3” – 6141630 4” - 6141632 90º Elbows: (Plain End / Belled End) 1” – 5133825 / 5233825 1 ½” – 5133827 / 5233827 2” – 5133828 / 5233828 3” – 5133830 / 5233830 4” – 5133832 / 5233832 45º Elbows: (Plain End / Belled End) 1” – 5133765 / 5233765 1 ½” – 5133767 / 5233767 2” – 5133768 / 5233768 3” – 5133770 / 5233770 4” – 5133772 / 5233772 30º Elbows: (Plain End / Belled End) 1” – 5133745 / 5233745 1 ½” – 5133747 / 5233747 2” – 5133748 / 5233748 3” – 5133750 / 5233750 4” – 5133775 / 5233776 | 5/5/03 |  |
|  | Heritage Plastics | Standard Couplings: 1” – 59603 1 ½” – 59605 2” – 59606 3” – 59608 4” – 59610 90º Elbows: (Plain End / Belled End) 1” – 59590 / 59374 1 ½” – 59592 /59376 2” – 59593 / 59377 3” – 59595 / 59379 4” – 59597 / 59381 45º Elbows: (Plain End / Belled End) 1” – 59577 / 59386 1 ½” – 59579 / 59388 2” – 59580 / 59389 3” – 59582 / 59391 4” – 59584 / 59393 30º Elbows: (Plain End / Belled End) 1” – 59563 / 59367 1 ½” – 59565 / 59368 2” – 59566 / 60249 3” – 59568 / 60250 4” – 59570 / 59398 | 7/24/12 |  |
|  | IPEX / PW Eagle | Standard Couplings: 1” – EC20 / 077003 2” – EC35 / 077006 3” – EC45 / 077008 4” – EC55 / 077010 90º Elbows: (Plain End / Belled End) 1” – 068582 / 068422 2” – 068585 / 068425 3” – 068587 / 068427 4” – 068589 / 068429 45º Elbows: (Plain End / Belled End) 1” – 068602 / 068563 2” – 068605 / 068566 3” – 068607 / 068568 4” – 068609 / 068570 30º Elbows: (Plain End / Belled End) 1” – 068622 / EE2030 2” – 068625 / EE3530 3” – 068627 / EE4530 4” – 068629 / EE5530 | 12/22/05 |  |
|  | Plastic Trends / Royal Pipe Systems | Standard Couplings: 1” – E010100 1 ½” – E010150 2” – E010200 3” – E010300 4” – E010400 90º Elbows: (Plain End / Belled End) 1” – E018100 / E021100 1 ½” – E081850 / E 021150 2” – E018200 / E021200 3” – E018300 / E021300 4” – E018400 / E021400 45º Elbows: (Plain End / Belled End) 1” – E019100 / E022100 1 ½” – E0191500 / E022150 2” – E019200 / E022200 3” – E019300 / E022300 4” – E019400 / E022400 30º Elbows: (Plain End / Belled End) 1” – E020100 / E072100 1 ½” – E020150 / E072150 2” – E020200 / E072200 3” – E020300 / E072300 4” – E020400 / E072400 | 1/8/10 |  |
| Formerly Carlon | Prime Conduit | Standard Couplings: 1” – E940F 1 ½” – E940H 2” – E940J 3” – E940L 4” – E940N 90º Elbows: (Plain End / Belled End) 1” – UA9AF / UA9AFB 1 ½” – UA9AH / UA9AHB 2” – UA9AJ / UA9AJB 3” – UA9AL / UA9ALB 4” – UA9AN / UA9ANB 45º Elbows: (Plain End / Belled End) 1” – UA7AF / UA7AFB 1 ½” – UA7AH / UA7AHB 2” – UA7AJ / UA7AJB 3” – UA7AL / UA7ALB 4” – UA7AN / UA7ANB 30º Elbows: (Plain End / Belled End) 1” – UA6AF / UA6AFB 1 ½” – UA6AH / UA6AHB 2” – UA6AJ / UA6AJB 3” – UA6AL / UA6ALB 4” – UA6AN / UA6ANB 90º Elbows: (Special Radius) 2” – UA9FJB (36” radius) | 5/26/09 |  |

| RMC Conduit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Allied Tube & Conduit | 1” – 278895 1 ½” – 278911 2” – 278929 3” – 278945 4” – 278960 | 5/5/03 | Galvanized Rigid Conduit Used only for extension of existing RMC conduit |
|  | Sawhill Tubular Division | Steelduct 1” – 662535-19345-1 1 ½” – 662535-19347-5 2” – 662535-19349-9 3” – 662535-19351-2 4” – 662535-19353-6 | 4/11/00 |  |
|  | Western Tube & Conduit Corp | 1” – WTR3 1 ½” – WTR5 2” – WTR6 3” – WTR8 4” – WTR91 | 5/5/03 |  |
|  | Wheatland Tube | 1” – 05440 1 ½” – 05442 2” – 05443 3” – 05445 4” – 05447 | 5/5/03 |  |

| RMC Fittings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Conduit Pipe Products | Coupling Part Numbers 1 ½” – 00135 2” – 00136 3” – 00138 4” – 00140 90º Elbow Part Numbers 1 ½” – 00165 2” – 00166 3” – 00168 4” – 00170 45º Elbow Part Numbers 1 ½” – 00185 2” – 00186 3” – 00188 4” – 00190 | 5/5/03 | Galvanized Rigid Conduit fittings Used only for extension of existing RMC conduit |
|  | Picoma Industries | Couplings, 90º Elbow and 45º Elbow in sizes: 1 ½”, 2”, 3”, 4” | 5/5/03 |  |
|  | Sawhill Tubular Division | Steelduct (Right and Left Threaded) Coupling Part Numbers 4”x4” – 20997 90º Elbow Part Numbers 3” – 21276 4” – 21279 45º Elbow Part Numbers 3” – 21271 4” – 21273 | 4/10/01 4/11/00 |  |
|  | Shamrock Conduit Products | Coupling Part Numbers 1 ½” – 9001 2” – 0319 3” – 0321 4” – 0323 90º Elbow Part Numbers 1 ½” – 7746 2” – 7747 3” – 7749 4” – 7751 45º Elbow Part Numbers 1 ½” – 7654 2” – 7655 3” – 7657 4” – 7659 | 5/5/03 |  |

| RMC Bushings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Arlington Industries | 1 ½” – 454 2” – 455 3” – 457 4” – 459 | 1/11/02 | Copper lug with insulated throat constructed of malleable iron. Threaded type |
|  | Bridgeport | 1 ½” – 385 2” – 386 3” – 388 4” – 390 | 5/5/03 |  |
|  | Lazy-lug | 1” – GLL-3C-B 1 ½” – GLL-5C-B 2” – GLL-6C-B 3” – GLL-8C-B 4” – GLL-10C-B | 5/5/03 |  |
|  | OZ-Gedney | 1” – IBC-100L-4AC 1 ½” – IBC-150L-4AC 2” – IBC-200L-4AC 3” – IBC-300L-4AC 4” – IBC-400L-4AC | 7/2/03 |  |
|  | Regal Manufacturing | 1 ½” – 8225 2” – 8226 3” – 8228 4” – 8230 | 5/5/03 |  |
|  | Steel City / Thomas & Betts | 1 ½” – BG-805 2” – BG-806 3” – BG-808 4” – BH-810 | 5/5/03 |  |

| Bridge Expansion Couplings | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Cantex | 1” – 5144033 1 ½” – 5144035 2” – 5144036 3” – 5144038 4” – 5144040 | 5/5/03 |  |
| Formerly Carlon | Prime Conduit | 1” – E945F 1 ½” – E945H 2” – E945J 3” – E945L 4” – E945N | 5/5/03 |  |

### Controller Cabinet			Back to Traffic Signal Table of Contents						Back to Main

| Pole Mount Traffic Signal Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| For Maintenance Use Only/or as Specified | IDC / US Traffic Corp. | Model 336A – 2 doors Model 303 – 1 door | 5/5/03 5/5/03 |  |
|  | Phillips Sisson Ind. | Model 336 – 2 doors | 5/5/03 |  |
|  | Safetran | Model 336A – 2 doors Model 303/8 – 1 door | 5/5/03 5/5/03 |  |

| Pad Mount Traffic Signal Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| For Maintenance Use Only/or as Specified | McCain | Model 332 / M35378 | 10/12/11 |  |
|  | Phillips Sisson Ind. | Model 332 | 5/5/03 |  |
|  | Safetran | Model 332-OPKS | 5/5/03 |  |

| Single Input File Pad Mount Traffic Signal Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| For Maintenance Use Only/or as Specified | McCain | Model OP332SI w/ slide out battery drawer UPS Battery Drawer 6 | 10/12/11 |  |
| Double Pad Mount Traffic Signal Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| For Maintenance Use Only/or as Specified | McCain | Model 333JP-OPKS | 6/16/10 | These should be fabricated to “Overland Park Special” configurations |
|  | Safetran | Model 333SD-OPKS | 6/16/10 |  |

| Hybrid Double Pad Mount Traffic Signal Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Safetran | Model 333SD Hybrid-OPKS STCAB1746 – Std Brushed Alum. | 10/6/11 | Reliance Controls Corp (30 A, 4-prong) External Generator Receptacle if specified |

| Pad Mount DMS Sign Cabinet | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Safetran | Model 334-OPKS | 5/5/03 |  |

### Detection Systems			Back to Traffic Signal Table of Contents						Back to Main

| Microloop Probes | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Global Traffic Technologies bought out 3M | Global Traffic Technologies / 3M / Canoga | Model 701 w/40004 Micro loop Cable | 2/18/08 |  |

| Non-Invasive Vehicle Detectors Probes | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Global Traffic Technologies bought out 3M | Global Traffic Technologies / 3M | Model 702 Probes and Carriers Model 702 Installation Kit Canoga C800 Interface Scotchcast 3832 Splice Kit | 2/18/08 |  |

| Pedestrian Pushbuttons ADA Audible | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Polara | Navigator APS 9”x12” frame – EN49CN1-PY (std pole) NPA4X2-y (adapter for pedestal pole) | 1/23/13 | Red LED indicator Audible locator Auto volume adjustment for ambient noise levels EN4 – EZ Communicator Navigator 4 Wire system 9 – 9” x 12” Face Plate C – 9”x12” R10-3e Pushbutton Sign N – No Braille on Face Plate 1 – Custom Message (Recorded at Factory) PY – Yellow back and front housing |

| Pedestrian Pushbuttons | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Campbell Co | 4EVR 120 – X – No LED | 4/5/12 | Yellow body with sound on actuation NO LED Flash X = B for Black or Y for Yellow |
|  | Polara Engineering, Inc. | Bulldog Series Push Button Assembly – BDSP-010-X Pole Mount Adaptor – BDPM-X | 2/10/12 |  |

| Pre-empt Detectors | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Global Traffic Technologies bought out 3M | Global Traffic Technologies / 3M | Model 721 | 2/218/08 | Two Direction Single Channel |

| Pre-formed Loop Detectors | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Never-Fail Loop Systems | Model A – in or under asphalt Model C – in concrete or bridge decks Model F – in sawed grooves in asphalt | 6/6/00 |  |

| Advance Radar Detectors | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Wavetronix | Model WX-SS-200V SmartSensor Advance Unit Click! 222 Surge Protection Module Click!301 Serial to Ethernet Converter Click! 112 (2-Channel) Contact Closure WX-SS-704-xx (cable harness) Pre-Assembled 19” Rack: 2 sensors – WX-SS-B02-0003 4 sensors – WX-SS-B02-0002 | 1/10/11 | With Preassembled 19” rack |

| Vehicle Detectors | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Global Traffic Technologies bought out 3M | Global Traffic Technologies / 3M / Canoga | Model C922 – Two Channel Model C924 – Four Channel | 2/18/08 | It shall have TS2 status output available |
|  | Reno | Model C-1200-SS Series – Two Channel Model E-1200-SS Series – Four Channel | 2/10/12 |  |

| Video Detection Systems | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Econolite/Autoscope Solo Terra | ASOLOTERRA1S – Image Sensor ATIP1 – Interface Panel ATAPE – Access Point ASTCBL10 – Interface Cable Kit 33550G5 SDLC Cable Harness | 5/17/07 | Easy-Lock Harting Connector On-Board Ethernet Port SDLC Cable Harness for TS-2 Comm to ASC/3 – RM Controller |
| Used for Maintenance Replacements and with ITS Plus3, Inc Camera systems Only | Econolite/Autoscope Terra Rack Vision | AIS4HCRZOOMU0S – AIS Image Sensor AIPx – Camera Interface Panel Coaxial Cable RG59 Jumper Cables ARVTERRA1E – Processor Card 33550G5 SDLC Cable Harness | 5/17/07 | Easy-Lock Harting Connector x = number of cameras to be connected to the interface panel (1 to 6) On-Board Ethernet Port |
|  | ITS Plus3, Inc. | ITSP-SM120C Video Detection Camera – Mounts on top of signal head ITSP-IC120C Video Detection Camera – Mounts inside signal head (McCain, or Econolite heads only) | Under Trial and Review | Signal Mount Camera with 120V, Coax Communication. Specify with either Terra Rack Vision or Iteris rack mounted processor modules |

### Grounding Equipment			Back to Traffic Signal Table of Contents						Back to Main

| RJ-45 Data Protector | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Atlantic Scientific | Zonebarrier-24585 | 7/11/12 | Use with IP High Definition CCTV Cameras |
|  | Protection Technology Group / Transector | Model: TSJ-POE56 Part Number: 1101-1074 | 7/11/12 |  |

| Ground Rod | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Chance/Hubbell | ½” x 8’-0” Cat. No. C611380 ½” x 10’-0” Cat No. C611300 | 4/24/12 | ½” x 10’-0” long at poles and controller cabinet ½” x 8’-0” long at service boxes Copper clad steel core UL listed |
|  | Erico Inc. / Eritech | ½” x 8’-0” Cat. No. 611380 ½” x 10’-0” Cat. No. 611300 | 2/27/02 |  |
|  | ITTBlackburn | ½” x 8’-0” Cat. No. 5008 ½” x 10’-0” Cat No. 5010 | 5/5/03 |  |
|  | Josyln | ½” x 8’-0” Cat. No. J-8328 ½” x 10’-0” Cat No. J-8330 | 5/5/03 |  |
|  | Knight | ½” x 8’-0” Cat. No. ½” x 10’-0” Cat No. GRC 1210 | 5/5/03 |  |

| Ground Rod Clamp | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Burndy | GRC 12 – ½” rod GRC 34 – ¾” rod | 2/27/02 | Hex head set screw Copper alloy Long bearing surface UL listed |
|  | Erico Inc. / Eritech | HDC12 – ½” rod HDC34 – ¾” rod | 12/1/05 |  |
|  | ITT Blackburn | Type JAB-12H | 5/5/03 |  |

### Junction and Service Boxes 		Back to Traffic Signal Table of Contents						Back to Main

| Type I Junction Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001423TA (12” x 12” x 12”) | 1/11/01 | Logo to read “Traffic Signal” Cover to be ¾” min thick Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers |
|  | Carson Industries | HLW1212-12 – Box only HLW1212-P0 – Cover only | 6/29/04 |  |
|  | CDR | SB33-1212-12 – Box only SC30-1212-02 – Cover only SA33-1212-12 – Assembly | 5/19/95 |  |
|  | Highline | PHB121212 – Box only CHC1212SS – Cover only PHA121212SS2 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 121212PCC – Box only 1212PCC – Cover only 121212PC – Assembly | 10/17/11 |  |
|  | New Basis | PCB121212A04 – Box only PCC121215A04 – Cover only | 8/8/03 |  |
|  | Quazite | PC1212BA12 – Box only PC1212CA0046 – Cover only | 5/5/03 |  |

| Type II Junction Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001429TA (11”x18”x12”) | 7/30/01 | Logo to read “Traffic Signal” Cover to be 1 ¾” to 2” thick Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers |
|  | Carson Industries | H1118-12 – Box only H1118-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-1118-12 – Box only SC30-1118-02 – Cover only SA-33-1118-12 – Assembly | 5/19/95 |  |
|  | Highline | PHB111812 – Box only CHC1118SS – Cover only PHA111812SS2 - Assembly | 3/3/11 |  |
|  | Martin Enterprises | 111812PCB – Box only 1118PCC – Cover only 111812PC – Assembly | 10/17/11 |  |
|  | New Basis | PCB111812A04 – Box only PCC111815A04 – Cover only | 8/8/03 |  |
|  | Quazite | PG1118BA12 – Box only PG1118CA0046 – Cover only | 5/5/03 |  |

| Type III Junction Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001640TAPCX12 A6001640TAPCX18 (17” x 30” x 30”) (Stacked Units) | 9/16/03 | Logo to read “Traffic Signal” Cover to be 1 ¾” to 2” thick Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers Depth of box shall be 30” minimum. May be attained by stacking with no additional payment. |
|  | Carson Industries | H1730-12 – 12” Deep Box only H1730-18 – 18” Deep Box only H1730-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-1730-30 – Box only SC30-1730-02 – Cover only SA-33-1730-30 – Assembly | 8/8/03 |  |
|  | Highline | PHB173012 – 12” Deep Box only PHB173018 – 18” Deep Box only CHC1730HS – Cover only PHA17301218HS2 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 173030PCB – Box only 1730PCC – Cover only 173030PC – Assembly | 10/17/11 |  |
|  | New Basis | PCB173012A04 – 12” Deep Box only PCB173018A04 – 18” Deep Box only PCC173015A04 – Cover only | 8/8/03 |  |
|  | Quazite | PG1730BA30 – Box only PG1730CA0046 – Cover only | 5/5/03 |  |

| Round Service Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| SPECIAL USE ONLY | Armorcast | A6000182TX36 – Box only A6000181T – Cover only A600018TAX36 – Box and Cover | 8/7/03 | Logo to read “Traffic Signal” Cover to be 1” thick min. |
|  | CDR | SB10-2700-36 – Box only SC10-2700-02 – Cover only | 5/5/03 |  |
|  | Quazite | LR2732BA36 – Box only PR2700CA0046 – Cover only | 5/5/03 |  |

| Type I Service Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001974TAPCX24 (24” x 36”x 24”) | 8/7/03 | Logo to read “Traffic Signal” Cover to be 3” thick Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers |
|  | Carson Industries | H2436-24 – Box only H2436-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-2436-24 – Box only SC30-2436-03 – Cover only SA33-2436-24 – Assembly | 8/8/03 |  |
|  | Highline | PHB243624 – Box only CHC2436HS – Cover only PHA243624HS2 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 243624PCB – Box only 2436PCC – Cover only 243624PC – Assembly | 10/17/11 |  |
|  | New Basis | PCA243624A04 – Assembly PCB243624A04 – Box only PCC243615A04 – Cover only | 2/26/02 |  |
|  | Quazite | PG2436BA24 – Box only PG2436CA0046 – Cover only | 5/5/03 |  |

| Type II Service Box | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Armorcast | A6001430TAPCX24 (30” x 48”x 24”) | 8/7/03 | Logo to read “Traffic Signal” Cover to be 3” thick two-piece underlapping Straight wall No mouseholes 3/8” – 16 NC hex head bolts and washers |
|  | Carson Industries | H3048-24 – Box only H3048-P1 – Cover only | 6/29/04 |  |
|  | CDR | SB33-3048-24W – Box only SC30-3048-23W – Cover only SA33-3048-24W – Assembly | 8/8/03 |  |
|  | Highline | PHB304824 – Box only CHC3048HS-2PC – Cover only PHA304824HS4 – Assembly | 3/3/11 |  |
|  | Martin Enterprises | 304824PCB – Box only 3048PCC – Cover only 304824PC – Assembly | 10/17/11 |  |
|  | New Basis | PCA304824A04 – Assembly PCB304824A04 – Box only PCC304815A14 – Cover only | 2/26/02 |  |
|  | Quazite | PG3048BA24 – Box only PG3048CC0046 – Cover only | 5/5/03 |  |

### LED Units	 				Back to Traffic Signal Table of Contents						Back to Main

| Red Ball LED | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | DuraLED 433-1210-003XL | 4/30/10 | Tinted or clear lens is acceptable Incandescent look |
|  | GELcore | DR6-RTFB-17A | 9/19/02 |  |

| Yellow Ball LED | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | DuraLED 433-3230-901XL | 4/30/10 | Tinted or clear lens is acceptable Incandescent look |
|  | GELcore | DR6-YTFB-17A | 9/19/02 |  |

| Green Ball LED | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | DuraLED 433-2220-001XL | 4/30/10 | Tinted or clear lens is acceptable Incandescent look |
|  | GELcore | DR6-GTFB-17A | 9/19/02 |  |

| Pedestrian LED | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Used for Maintenance Applications Only | DiaLight | 430-6472-001X | 4/30/10 | 16” X 18” Orange Hand/White Man Filled/Overlay Style Incandescent look |
|  | GELcore | PS7-CFL1-01A (LED look) | 9/19/02 |  |

| Countdown Pedestrian LED | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | 430-6479-001X | 4/30/10 | 16” X 18” Orange Hand/White Man Incandescent look Filled/Overlay Style 9” Numerals |
|  | GELcore | PS7-CFF1-26A | 2/16/06 |  |

| Red LED Arrow | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | 432-1314-001XOD | 4/30/10 | Tinted or clear lens is acceptable Incandescent look |
|  | GELcore | DR6-RTAAN-17A | 9/19/02 |  |

| Yellow LED Arrow | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | 431-3334-901XOD | 4/30/10 | Tinted or clear lens is acceptable Incandescent look |
|  | GELcore | DR6-YTAAN-17A | 9/19/02 |  |

| Green LED Arrow | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | 432-2324-001XOD | 4/30/10 | Tinted or clear lens is acceptable Incandescent look |
|  | GELcore | DR6-GTAAN-17A | 9/19/02 |  |

| Bi-Modal Green/Yellow LED Arrow | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | DiaLight | 430-6370-001 | 4/30/10 | Clear Lens, pixilated arrow |
|  | GELcore | DR6-ECA6-21A | 9/19/02 |  |

### Loop Sealants 				Back to Traffic Signal Table of Contents						Back to Main

| Loop Sealants | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | 3M | Black 5000 | 5/5/03 | Crafco sealant may only be used on loops sawed into the final surface of the pavement. |
|  | Bondo Traffic | E-709 or E-709-CP | 5/5/03 |  |
|  | Chemque | Q-Seal 290S Grey or Black | 10/23/03 |  |
|  | Crafco Inc | RoadSaver 221, Part No. 34221 | 5/5/03 |  |
|  | Ruscoe Highway Products | PS-2000 – Comes in Gray or Black | 7/10/00 |  |

### Miscellaneous Controller

### Equipment					Back to Traffic Signal Table of Contents						Back to Main

| 170 Controller | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Quixote Traffic Corp purchased US Traffic | IDC / US Traffic Corp / Quixote Traffic Corp | 170E | 5/503 | USED ONLY FOR MAINTENANCE |
|  | Safetran | 170E | 5/5/03 |  |

| Rack Mount Controller | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Safetran/Econolite Control Products, Inc. | Model ASC/3 RM 61110100000 | 1/27/11 | with Data Key Modules:  1 – 3B front panel  1 – 2A field panel  1 – 4A power supply  1 – 1B CPU module Removable power cord Meets CalTrans Transportation Electrical Equipment Specifications August 2002 as revised October 27, 2003 ASC/2070 Firmware 1.03.02 shall be provided with the controller |

| Bus Interface Unit (BIU) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Safetran | 160-1003-505 | 10/6/11 | Only used with Hybrid Cabinet |

| AC Isolator | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | TSC / Traffic Sensor Corp | TSC 252 | 5/5/03 | Model 252 |
|  | GDI / General Devices & Instruments | ACIM252 | 5/5/03 |  |
|  | PDC / Power Distribution Control | ACI-88 Model 252 | 5/5/03 |  |

| Conflict Monitor | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | EDI / Eberle Design, Inc. | 2018 KCLip – (Std 332 Cabinet) with Datakey programming and Ethernet port | 2/19/09 | Not used with Hybrid Cabinet. See “Malfunction Management Unit” below. |

| DC Isolator | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | GDI / General Devices & Instruments | DIM242 | 5/5/03 | Model 242 Not used with Hybrid Cabinet. See “Detector Test Switch Module” below. |
|  | PDC / Power Distribution Control | DCI-82 Model 242 | 5/5/03 |  |
|  | TSC / Traffic Sensor Corp | TSC 242 | 5/5/03 |  |

| Detector Test Switch Module | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Econolite | 35280G1 | 2/10/11 | Only used with Hybrid Cabinet instead of 242 DC Isolator |

| Flash Transfer Relay | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | CII Technologies / MidTex | MidTex 136-62T3A1 | 5/5/03 | Model 430 |
|  | Magnecraft | W21ACPX-2 | 5/5/03 |  |
|  | Reno A&E | TR-200 | 11/3/05 |  |

| Flasher Unit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | EDI / Eberle Design, Inc. | EDI 204 | 5/5/03 | Model 204 |
|  | TSC / Traffic Sensor Corp | TSC 204 | 5/5/03 |  |
|  | GDI / General Devices & Instruments | FL204 | 5/5/03 |  |
|  | PDC / Power Distribution Control | SSF-88 | 5/5/03 |  |
|  | Reno A&E | FL-200 | 11/3/05 |  |

| Malfunction Management Unit (MMU) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Eberle Design Inc. | MMU2-16-LE(ip) | 1/10/13 | Only used in Hybrid traffic signal cabinet in place of the conflict monitor |

| Power Distribution Surge Protection Unit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Atlantic Scientific | 35326 (CPS-1215RMS) | 10/28/08 | Room for 8 transformer spaced outlets (minimum) 15 amp breaker Rack mounted NEMA 5-15 |
|  | Geist Manufacturing, Inc. | SPX084-10 | 11/4/05 |  |

| Power Supply | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | EDI | Model 206L | 7/9/10 | High efficiency power saving w/ solid state transfer relay |

| Power Distribution Assembly (PDA) | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | McCain | PDA#2 M63186 | 7/14/10 |  |
|  | SafeTran |  |  |  |

| Pre-empt Phase Selectors / Discriminator Module | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| Global Traffic Technologies bought out 3M | Global Traffic Technologies | Model 762 – Two Channel Model 764 – Four Channel | 4/19/11 | With Ethernet Ports |

| Switchpack / Load Switch | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | EDI / Eberle Design, Inc. | EDI 200 | 5/5/03 | Model 200 |
|  | GDI / General Devices & Instruments | LS200 | 5/5/03 |  |
| Quixote Traffic Corp purchased US Traffic | IDC / US Traffic Corp / Peek Traffic / Quixote Traffic Corp | 200 | 5/5/03 |  |
|  | PDC / Power Distribution Control | SSS-88 | 5/5/03 |  |
|  | Reno A&E | LS-200 | 11/3/05 |  |
|  | TSC / Traffic Sensor Corp | TSC200 | 5/5/03 |  |

| Surge Protector | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Edco | SHA-1250 | 8/5/10 |  |
|  | MVC Inc | ICP-110S | 7/9/10 |  |

| Video Surge Protection Unit | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | EDCO | CX06BNCY | 8/8/01 | Note: Not required for the Ecololite Autoscope System. |

### Mounting Brackets 			Back to Traffic Signal Table of Contents						Back to Main

| Video Detection Camera Mounting Bracket for Luminaire Arm | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | SH-0502-10 w/ SE-4049 SH-0509-10 w/SE4049 Econolite | 10/4/02 | Narrow hub plate substituted for SE-4071 universal hub plate |
|  | PELCO | EM-1109 EM-2200 | 10/31/05 | The EM-1109 is for mounting on top of the luminaire arm The Em-2200 is a J-hook designed to mount below the luminaire arm |

| Video Detection Camera Mounting Bracket Side of Pole Mount | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco | EM-2000 | 10/31/05 |  |

| Video Detection Camera Mounting Bracket for Mast Arm | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AstroBrac AS-0175-5-62 | 10/4/02 |  |

| Combined Video Detection Camera /Signal Head Mounting Bracket for Mast Arm | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AstroBrac AB-0608-74-L (4 Section) |  |  |

| Radar Detector Mounting Bracket for Mast Arm | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AstroBrac SP-5772-PNC | 7/24/12 | 12 = Tube Length 84 = Cable Length P = Paint NC = No Coating |

| RWIS Sensor Mounting Bracket for Mast Arm | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AstroBrac AB-0164-12-84 | 1/28/11 | With 4-hole mounting plate 12 = Tube Length 84 = Cable Length (RWIS Manufacturer provides the PVC enclosure that mounts to the Tee pipe nipple) |

| Combined Radar Detector / RWIS Sensor Mounting Bracket for Mast Arm | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | AstroBrac AB-0164-23-84 (SPECIAL) and SH0515 | 1/28/11 | With 4-hole mounting plate 23 = Tube Length 84 = Cable Length “SPECIAL” indicates the tube is threaded on each end The SH0515 mounting bracket for the radar unit needs to be drilled for a 5 hole configuration. An additional SH0515 mounting bracket is attached to the other threaded end for the RWIS unit. Only one Tee pipe nipple is required (RWIS Manufacturer provides the PVC enclosure that mounts to the Tee pipe nipple) |

| Mast Arm Signal Head Bracket | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | Astro Brac AB-0125-1-L (1-Section) Astro Brac AB-0125-3-L (3-Section) Astro Brac AB-0125-4-L (4-Section) | 5/5/03 | Cable mount bracket assembly |

| Side Mount Signal Head Bracket | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Auto/Eagle | UKS-1452X | 5/5/03 | Yellow polycarbonate X=Y for Yellow X= B for Black |
|  | Component Products, Inc. | TSP880-X | 5/5/03 |  |
|  | Gades | UKS1452X / PDM-405 | 5/5/03 |  |

| Pedestrian Head Bracket | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | McCain Traffic Supply | M27168 | 5/5/03 |  |

| Mini Pre-empt Detector Bracket | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Pelco Products, Inc. | Astro Brac AB-0163-L | 12/29/04 | Cable mount |

### Poles						Back to Traffic Signal Table of Contents						Back to Main

| Galvanized Steel Signal Poles | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Union Metal | 50915-B1 w/ Rev 05 (Y1 through Y121) | 10/27/04 | Shall meet 1994 AASHTO Criteria |
|  | Valmont | DB00175 Rev D dated 3/25/88 | 3/4/03 |  |

| Aluminum Pedestal Poles | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Component Products, Inc | Pedestal Base CPI-BAS-1 Pole Cap CPI-APC-1 9’ Pedestal Pole CPI-AP-9-40 13’ Pedestal Pole CPI-AP-13-40 14’ Pedestal Pole CPI-AP-14-40 | 5/5/03 | Set screws required in base collar Include 2 7/8” OD x 7/8” ID galvanized flat washers |
|  | Gades Sales | Pole Cap PC4.5 9’ Pedestal Pole, PB5100-9 13’ Pedestal Pole, PB5100-13 14’ Pedestal Pole, PB5100-14 | 5/5/03 |  |
|  | Pelco | Pedestal Base PB-5335-1S-GL Pole Cap PB-5402 9’ Pedestal Pole PB-5100-9 13’ Pedestal Pole PB-5100-13 14’ Pedestal Pole PB-5100-14 | 5/5/03 |  |

### Power Backup Systems	 	Back to Traffic Signal Table of Contents						Back to Main

| CNG Generators | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Alpha Technologies | AlphaGen CE-3x2-50-48 NG with Cold Weather Starting Kit With PCC-3x Polymer Concrete Pre-Cast Pad Includes Alpha supplied battery DO NOT PROVIDE WITH TRANSFORMER AND FUSE | 6/17/03 | 48V DC output voltage 96 amp max DC output current 10.5 Hp single OHV engine 13.5 VDC Ignition Charger Voltage 6 amp max Ignition Charger Current 2800 to 3600 RPM variable speed 80 CuFt/hr Natural Gas, 1000 BTU/CuFt 0.5 – 2 PSI Gas Inlet Pressure |

| UPS Systems | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
| For Maintenance Use Only | Alpha | Novus FXM-1100 – Part No. 017-230-23 (48-volt system) with Automatic Transfer Switch and AC receptacle P/N 02016827 | 11/10/11 | Ethernet port capabilities See Battery requirements below. Use ONLY the specified batteries as listed for each UPS system as listed in the table below. |
|  | Clary Stand Alone Battery Backup Unit | SP 1250-PD-N – Uninterruptible Traffic System with Integrated PIM and Programmable Display SPO-09A2 – SNMP Adapter with cables manual and software SPD-302C – Bypass Switch with GFCI and Generator Plug SP-19N1 – Battery Cable 72-volt system | 9/3/09 |  |
|  | Clary Combined Battery and CNG Backup Unit | SP 1250-PD-N-48 – Uninterruptible Traffic System with Integrated PIM and Programmable Display SPO-09A2 – SNMP Adapter with cables manual and software SPD-302C – Bypass Switch with GFCI and Generator Plug 100-16136 – 48 VDC Battery Generator Interface Box 104-16163-60 – 48 Volt Dual String Battery Cable 48-volt system | 4/12/10 |  |

| Power Transfer Switches | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Gen/Tran Corporation | TS300230PL | 10/5/05 | Double Pole 30 Amp manual transfer switch Aluminum housing and #2 key Pilot light indicator |

| Batteries | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Alpha | Model 165 GXL – Part No. 1810015 (set of four batteries) 48-volt system (Stand alone or combined BBS/CNG) | 1/18/12 | Gel Top Terminal Battery (4 Year Full Replacement Warranty) |
|  | Clary | OP72C-41 – Batteries (set of six) 72-volt system (Stand alone BBS) OP96C-41 – Batteries (set of eight) 48-volt system (Combined BBS/CNG) | 10/7/11 | Absorbed Glass Mat (AGM) Valve Regulated , Lead Acid (VRLA) |

### Secondary Service Pedestals 	Back to Traffic Signal Table of Contents						Back to Main

| Aluminum Electrical Service Enclosure | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Myers Custom Products, Inc. | MEA-IIVLM-TSR – new part number – drawings have been approved but physical review of product is pending |  | 0.125” Aluminum, 30 amp breaker Corbin #2 lock on door No photocell or lighting relays Ringless Meter Socket with Horn By-Pass |
|  | Pacific Utility Products | USP2R-100-112C-OPK-TS | 2/17/12 |  |

| Battery Backup / Electrical Service Enclosure | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Myers Custom Products, Inc. | Cabinet – MET2-PB-M030-AC-EMI Drawing No. F518506 | 8/23/05 | 0.125” aluminum Manual transfer switch behind police door For use with external portable generator See below for External Generator Receptacle data 20Amp breaker for CCTV Camera Disconnect |
|  | Pacific Utility Products | Cabinet – USP29-57-BBS | 7/9/10 |  |
|  | Traffic Signal Controls | Cabinet – 2116UPME1401 | 9/3/09 |  |

| Battery Backup to CNG Electrical Service Enclosure | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Myers Custom Products, Inc. | Cabinet – MET2-PB-M030-DC-EMI Drawing No. F518507 | 8/23/05 | 0.125” aluminum For use with permanent CNG generator and gas service line 20Amp breaker for CCTV Camera Disconnect |
|  | Pacific Utility Products | Cabinet – USP29-57-BBS | 7/9/10 |  |
|  | Traffic Signal Controls | Cabinet-2116UPME1401 | 9/3/09 |  |

| CNG External Generator Receptacle | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Hubbell | HBL2710SW including HBL2715 flanged receptacle | 4/2/12 | Twist Lock Recessed Male, 30 Amp 120/240 Volt, 4 prong including ground with outdoor hinged cover |
|  | Reliance Controls | PK30 Power Inlet Kit, including L1430F flanged receptacle | 4/2/12 |  |

### Signal Heads				Back to Traffic Signal Table of Contents						Back to Main

| Vehicular Signal Heads | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | Automatic Signal / Eagle Signal | SA103A1111YBB for 3 Section SA104A1111YBB for 4 Section SA101A1111YBB for 1 Section | 5/5/03 | Yellow Polycarbonate Body (Standard) Black Polycarbonate Body (Special) Black Polycarbonate Doors and Visors Visors to be Tunnel Type LED retrofit 12” Sections |
|  | Econolite Control Products, Inc. | TP31VJC2P0H0 for 3 Section Yellow TP41VJC2P0H0 for 4 Section Yellow TP11VJC2P0H0 for 1 Section Yellow TP31VJF2P0H0 for 3 Section Black TP41VJF2P0H0 for 4 Section Black TP11VJF2P0H0 for 1 Section Black | 5/9/03 |  |
|  | Indicator Controls Corp |  | 6/4/01 |  |
|  | McCain Traffic Supply | MTSTP-1X-6-XX-MMP1213PB for 1 Section MTSTP-3X-6-XX-MMP1213PB for 3 Section MTSTP-4X-6-XX-MMP1213PB for 4 Section | 5/5/05 |  |
| Quixote Traffic Corp purchased US Traffic | Peek Traffic / Quixote Traffic Corp | PSS83S003FO for 3 Section PSS84S004FO for 4 Section | 5/5/03 |  |

| Countdown Pedestrian Signal Heads | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | McCain Traffic Supply | M69916 – Yellow housing M69161 – Black housing | 12/30/04 | Yellow polycarbonate body (Standard) Black polycarbonate body (Special) Black Aluminum Door / No Z-Crate Visor |
|  | Siemens | Left: SG7MZ12COYB010-49 Right: SG7MZ11COYB010-49 | 9/20/11 |  |

### Wire Connectors				Back to Traffic Signal Table of Contents						Back to Main

| Wire Connectors for Loop Lead-In | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | King Innovation/Dryconn | KB – Aqua/Blue Waterproof Connector 62310 – Card of 3 62325 – Bag of 15 62335 – Bag of 50 62340 – 250 | 10/14/03 | Wire Range: Min. #14 / Max. #6 Copper Silicone Sealant Filled Watertight/raintight |

| Wire Connectors for Multi-Conductor Signal Cable | Manufacturer | Catalog Number | Approval Date | Comments |
| --- | --- | --- | --- | --- |
|  | King Innovation/Dryconn | King 6 Blue Waterproof Connector 10600 – Card of 2 10666 – Bag of 10 | 10/14/03 | Wire Range: Min. #22 / Max. #8 Copper Silicone Sealant Filled Direct Burial |